## Slide 1
Lecture Unit
Introduction Finite Element Analysis (FEA) with Ansys MechanicalTM Software– 2D/3D Elements
Developed by
Rasul Abdusalamov & Prof. Dr.-Ing. Mikhail Itskov
http://www.km.rwth-aachen.de/
Curated by the Ansys Academic Team
Notes: Lecture Unit – Introduction to Finite Element Analysis (FEA) with Ansys Mechanical Software– 2D and 3D elements
In computational Finite Element Analysis (FEA), numerical calculations are used to solve complex engineering problems by breaking down a structure into smaller, finite elements. Each element represents a small portion of the structure, where equations based on physical laws (such as equilibrium, compatibility, and material behavior) are applied. The software assembles these equations into a large system that represents the entire structure. By solving this system of equations, FEA predicts how the structure will respond to various loads, stresses, and boundary conditions, providing detailed insights into its performance and safety.
In this lecture unit, Introduction to Finite Element Analysis (FEA) with Ansys Mechanical Software, we will particularly study 2D and 3D elements, from transforming a solid model into a FEA model by meshing its geometry to solving the problem with its specific boundary conditions.
Next slide: Intended learning outcomes for this lecture unit, used resources and further information.

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of 2D and 3D FEA
Skills and Abilities | Ability to use the Ansys Mechanical software to set up 2D and 3D structural simulations
Values and Attitudes | Awareness of the importance of simulation in engineering design
In-Built Assessment
  Exercises:
  Quizzes
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Resources
  Software: Ansys MechanicalTM 2024 R2
  Images: Ansys Inc.
  Source: RWTH Aachen – Department of Continuum Mechanics (PIFEM-Marathon)
  Textbook: Finite Element Modeling and Simulation with ANSYS Workbench (2nd Ed.); Bridge Engineering Handbook: CRC Press, 2000.
Ansys software mentioned | Ansys MechanicalTM, a structural finite element analysis software Ansys Workbench™, a simulation integration platform
Notes: Learning Objectives
This lecture unit is aimed at teaching the fundamental concepts of FEA in 2D and 3D analyses in mechanical engineering and consolidates the understanding by employing the finite element analysis software Ansys Mechanical.
The resources used in this lecture and for further reading/information are listed and mentioned in specific slides through the lecture.
In-Built Assessment: Through this lecture, there are some moments with quizzes and exercises that are mentioned with the following icons.
Next slide: Outline of lecture unit – Briefly presents the topics that will be discussed through the lecture.

## Slide 3: Outline of Lecture Unit
Numerical & Structural Analysis:
  Methods for Solving Engineering Problems
  From Physical Problem to Final Product
Meshing & Solver:
  Overview in Mesh Quality Methods and Parameters
  Boundary Conditions and Results
2D Structural Analysis – Plane Elements and Simulation with Thin-Walled Structures
3D Structural Analysis – A practical Workflow from Geometry to Analysis and Validation
Notes: Outline of lecture unit
In this lecture about 2D and 3D elements in Finite Element Analysis (FEA), we will discuss some key topics to achieve a good comprehension in the concepts of Numerical and Structural Analysis, exploring methods for solving engineering problems by following a workflow starting from the physical problem to the final product. However, before understanding how to add the physical conditions and get results for deformation or stress, for example, it is necessary to deepen into the concept of meshing – What are nodes and elements? What shapes and types of elements it is possible to work with? What is the difference between surface and solid elements? How is it possible to get a mesh of a better quality (refine)?
After that, it will be possible to learn the process of setting boundary conditions and run the simulation by adding an analysis – such as Total Deformation, Equivalent Stress, Force Reaction, etc. In this lecture, we will focus on Static Structural simulations but highlighting the differences between 2D and 3D analysis. When is it recommended to choose one over another? What are the differences in the geometry, in the mesh and in the workflow through Ansys Workbench platform?
This lecture counts with 5 exercises to practice the achieved knowledge – one focused on mesh quality, 2 related to 2D analysis and 2 related to 3D analysis. Some slides also count with additional reading to allow the discussion to go further.
Next slide: We will discuss about the differences of experimental, numerical and analytical methods.

## Slide 4: Numerical Analysis – Methods for Solving Engineering Problems
Analytical Methods
Different methodologies available
Used mainly for simple idealized cases
Time-consuming approach for complex problems
Numerical Methods
Finite Element Analysis is predominant
Iterative algorithm suitable for computers
Fast solutions to complex problems
Experimental Methods
Prerequisite to many numerical simulations
Follow standardized test regimes
Time- and cost-consuming approach to data acquisition
Notes: Structural Analysis – Methods for solving engineering problems
Structural Analyses are carried out to understand the behaviour of structures when forces are exerted on them. Two key state variables that help engineers and designers assess the structural performance and behaviour of parts are stresses and strains. To determine those, three methods are at one's disposal: (a) Analytical, (b) numerical and (c) experimental. *Click*
Experimental methods are methods in which the design is manufactured in real life and tests are then carried out. These methods are required to calibrate and validate simulation models at important phases of development. Experimental methods are generally standardized tests. They are time consuming and can often be very expensive to create and analyze. *Click*
Numerical methods are simplified iterative algebraic equations that can be solved by a computer in order to obtain results. Finite Element Method is predominantly used in analyzing engineering problems as can be easily implemented in computers. In this lecture unit we will be using Ansys tool, which uses finite element methods to solve engineering problems. *Click*
Analytical solutions are exact and are often performed with hand calculations. Several methods are available in structural mechanics theory and will not be the object of this lecture unit. However, these exact solutions can only be found for simple idealized problems while for most engineering problems it would be problematic to be solved analytically because the models are too complex (for example from a geometrical perspective). *Click*
In this lecture unit we will focus on the numerical and analytical methods.
In the next slide we will specifically look at how FEA compares/compliments analytical solutions.

## Slide 5: Numerical Analysis – Methods for Solving Engineering Problems
Numerical Methods
Analytical Methods
Engineering Problem
Complexity
low
high
…
…
Solution
Method
Notes: Structural Analysis – Methods for solving engineering problems
While analytical solutions can be easily and quickly found for simple geometries and load conditions through simplification and idealization of the problem, numerical methods are required to obtain solutions for complex geometries, loading conditions and material properties (e.g. non-isotropic properties, multi-material composites, etc.) for which analytical solutions are difficult and time-consuming to obtain.
Let’s expand on the question of ‘Why to use FEA’ in the next slide.

## Slide 6: Numerical Analysis – Finite Element Analysis (FEA) and Method (FEM)
FEM is the mathematical method used to conduct a FEA, in which partial differential equations are solved to describe physical phenomena.
FEA are performed using FEM, which are implemented in CAE (computer-aided engineering) tools, providing a solution for virtual prototyping.
FEA helps to solve structural, heat transfer, fluid flow or electromagnetic problems quickly by exploiting computational power and make design changes early product development stage.
eliminate risk
increase quality
drive innovation
reduce costs
lower design cycle time
manage complexity
FEA-simulations enable you to
Finite
Element
Analysis
Finite
Element
Method
Numerical technique
Type of analysis
Notes: Finite Element Analysis (FEA) or Method (FEM)
FEM is the mathematical method used to conduct FEAs, in which partial differential equations are solved to describe physical phenomena.
FEA are performed using FEM, which are implemented in CAE (computer-aided engineering) tools, providing a solution for virtual prototyping.
FEA helps to solve structural, heat transfer, fluid flow or electromagnetic problems quickly by exploiting computational power and make design changes early product development stage.
FEA enables:
Innovation – design exploration through parameterization, optimization (e.g. Topology optimization) and general multi-physics simulation.
Cost reduction – focus in virtual rather than costly physical testing).
Management of complexity in design and physics.
Improve quality – validate design and analyze it for various conditions to ensure consistent performance.
Reduction in cycle time – product-to-market time is reduced as R&D through simulation is significantly faster than through physical testing and design iterations.
Risk reduction – Identify weak spots, e.g. for repeated/fatigue loading which may not be visible from experimental tests (e.g. crack formation). Note: These presupposes are correct numerical mode; in most cases prototyping is still mandatory.
No simulation substitutes physical testing, but it significantly accelerates the time required to reaching to a mature product stage and lowers the likelihood of additional design iterations.
Let’s expand on the question of ‘What FEA is’ in the next slide.

## Slide 7: Numerical Analysis – Finite Element Analysis (FEA) and Method (FEM)
FEM is a numerical method that exploits computational power to calculate solutions for a range of different engineering problems, offering good approximate solution to complex problems in the field of e.g. solid mechanics (e.g., statics and dynamics).
Element type: Tetrahedron
node
At the core of FEM lies the discretization, which means a model is divided into a finite number of smaller bodies or elements that are connected at common points, the so-called nodes. The quality of the solution depends on the size and type of the used elements.
Each node has a limited number of degrees of freedom (DoFs), so e.g. a continuum solid becomes discretized into a finite number of DoFs, based on the number and type of elements.
For each of those elements a set of algebraic equations are solved in an iterative fashion.
Notes: Finite Element Analysis (FEA) or Method (FEM)
FEA is a numerical method that exploits computational power to calculate solutions for a range of different engineering problems (see next slide for examples). It offers e.g. good approximate solution to complex problems in the field of solid mechanics (e.g., statics and dynamics).
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies or elements that are connected at common points, the so-called nodes. The quality of the approximated solution depends on the size and type of the elements in use. *Note: For this lecture unit on 2D/3D analysis, meshing will be dealt with in detail.
Each node has a limited number of degrees of freedom (DoFs), so e.g. a continuum solid becomes discretized into a finite number of DoFs, based on the number and type of elements. The more elements and nodes are used to model an object, the higher the accuracy.
For each of those elements a set of algebraic equations are solved in an iterative fashion.
The governing equations of FEAs are differential equations and boundary conditions which will be addressed in the next slide.

## Slide 8: Numerical Analysis – From Physical Problem to Final Product
Physical Problem
Numerical Model
Physical Prototype
Final Product
Fluid Mechanics
…
e.g. bracket
e.g. pipe
e.g. heat sink
Physical principles
System of algebraic equations
Governing equations
Boundary conditions
Euler-Bernoulli beam deflection
SM
Navier-Stokes motion of viscous fluids
FM
Fourier’s law of heat transfer
TA
Insulation at x=0
TA
Parallel flow
FM
Fixed end
SM
SM
FEA approximate
Stiffness matrix
Nodal vector (disp.)
Force vector
Solid Mechanics
Thermal Analysis
Notes: Structural Analysis – From Physical Problem to Final Product
There exist many physical problems in the field of solid and fluid mechanics as well as thermal (heat transfer) mechanics that can be solved using numerical methods like FEA.
Engineering/physical problems and their associated phenomena can be expressed as a numerical model through governing equations and boundary conditions.
- Solid Mechanics: e.g. Euler-Bernoulli beam deflection with a fixed end as boundary condition
- Fluid Mechanics: e.g. Navier-Stokes motion of viscous fluids with a parallel flow boundary condition
- Thermal Analysis: e.g. Fourier’s law of heat transfer with a local insulation boundary condition
In case of a structural mechanics problem, FEA approximates the displacement of the beam based upon the applied force and the stiffness matrix, which is directly linked to the material’s Young’s modulus. The nodal vector for the displacement is given for some nodes for which a boundary condition is defined (here: fixed end), the other can be determined by creating the inverse of the stiffness matrix (Note: this is an elaborate process to conduct analytically, which is why it lends itself to exploit the computational performance for this purpose). Now, the more elements you use to represent the beam, the more nodal displacements will be calculated along its length and the better you will be able to determine the deflection curve.
The next slide summarizes what are the steps for a structural analysis.

## Slide 9: Structural Analysis – FEA Workflow
Physical Problem
Numerical Model
Physical Prototype
Final Product
Pre-processing
Post-processing
Geometry and Material
Validation
Boundary conditions (e.g. supports, forces, etc.) and analysis type (e.g. structural, modal, thermal, etc. analysis)
CAD-geometry (e.g. shape, cross-sections, assemblies) and material (e.g. steel, rubber, wood, etc.)
Numerical solution (i.e. approximation) to the system of equations at selected points obtained using FEA
Sanity check (i.e.
do the results match the expectation, are the results plausible?)
Evaluation of outputs/state variables (e.g. displacement, stresses and strains)
Mathematical model
Physical principles
Notes: Structural Analysis – FEA Workflow
Structural Analysis is carried out in order to understand the behaviour of structures when forces are exerted on them.
This structural analysis methodology can be summarised through the following steps:
*Click*
The process starts off with designing the geometry and defining the material of our structure. *Click*
Pre-processing involves defining the boundary conditions. These include loading conditions (like force, torsion, etc.) and supports (like fixed, hinged, etc.), and connecting mechanisms. *Click*
Once the geometry and loading conditions have been setup the appropriate method to solve the problem needs to be decided. This can be analytical also known as hand-calculation, which means the exact solution is found for the problem or numerical, such as the Finite Element Method which are approximate solution computed by computers. The selection of the method depends on the model complexity and the available resources. *Click*
Once the problem has been solved, we move on to postprocessing. Here the required outputs like displacement, stress and strain can be gathered and evaluated. *Click*
The last but important step, which is too often forgotten, is to validate the resulting outputs and check if they make sense. For example, are the magnitude of the results in the expected range or are they too large or too small, does the analytical solution and numerical solution match? Is the quality of the results predicted from the mesh for the stress/strain gradients observed?
As the wheel schema suggests, this process can be iterative and can take several cycles of repetition before the required end results are met. This can be very different and depend on design requirements, cost constraints, weight limitation, etc.
In the next slide, the underlying assumptions and equations of FEA will be discussed.

## Slide 10: Structural Analysis – FEA Basic Equations
Equilibrium
Internal stresses and must be in equilibrium everywhere which presupposes a local equilibrium (i.e. the sum of all forces is zero).
Compatibility
Apart from cracks in a structure, displacements/strains must continuous if the structure is continuous.
Constitutive Laws
The constitutive material behavior (stress-strain and strain-displacement relationship) must be satisfied.
Body and surface forces
Displacements
Stresses
Strains
*
Note: Capital letters generally refer to the global and lowercase letters to the element matrix.
* Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
† Intro to Material Elasticity - ANSYS Innovation Courses
†
Notes: Structural Analysis – Basic Equations
To solve structural solid mechanics problem requires the three basic equations must be satisfied:
Equilibrium,
Constitutive Laws and
Compatibility.
The equilibrium condition for static but also dynamic problem states that the sum of all forces must be zero, i.e. the internal stresses of a component are in equilibrium. Here, the body and surface forces are being considered and linked to the stresses and strains. As will be shown later, three equilibrium conditions define the six components of stress or strain in an infinitesimal element. (Note: In the next couple of slides, the lecture unit will expand on the topic of equilibrium).
The constitutive laws define/approximate the stress-strain relationship of materials (Young’s and bulk modulus, Poisson’s ratio, yielding, hardening, etc.) as a result of an applied force. These relation can be phenomenological (derived from experiments) in nature or derived from first principles (also assumptions or postulates).
The compatibility condition ensures that a continuum body is deformed continuously without creating gaps, meaning compatibility is guaranteed between displacements and strains (i.e. displacements are obtained by integration of the strains). Important to note is that the displacements are considered the first nodal quantitates that are being determined in FEA; stresses and strains are secondary quantities that are expressed based upon the nodal displacements.
(*Click*)
The system of equations for a structural analysis is directly based upon those basic equations and relates the applied force vector F to the stiffness matrix K and displacement vector u. Note, the use of capital and lowercase letters in this equation is used to denote global or elemental (nodal) values.
Further reading & Equilibrium Condition: Additional free online courses/lecture notes on material elasticity and stresses and strains are linked. In the next couple of slides, the lecture unit will expand on the topic of equilibrium.
Next slide: Introduction to nonlinearities and their sources to understand when it’s possible to consider a linear behavior in a solid mechanics problem.

## Slide 11: Structural Analysis – Linear and Nonlinear FEM
Stiffness matrix
Force vector
Nodal vector (disp.)
All phenomena we see in nature have some degree of nonlinearity. To simplify various physical problems, it is common to assume linear relationships and present a solution that is sufficiently accurate, but still an approximation.
In the underlying system of equations in the linear analyses, it is possible to observe the relation between the force and the displacement, in which the stiffness matrix is constant. However, outside the material’s linear elastic region, for large deformations, the stiffness matrix is no longer constant, and the linear assumption cannot be applied.
Since the stiffness matrix is a function of its geometry and material properties, it is possible to highlight three main sources of non-linearity.
It is possible that the nonlinearities present in the model are a result of a combination of factors, not just one alone. Thus, it is important to analyse what is the main source of nonlinearity and think carefully, according to the wanted application, if it is possible to simplify the model to a linear comportment.
Contact nonlinearity
Contacts between parts of an assembly can introduce nonlinearity in a model, for example by relative motion or contact loss.
Nonlinear material
In the stress-strain curve, when the structure is stressed beyond its elastic limit (linear comportment), plasticity introduces nonlinearities to the model.
Introduction to nonlinearities – Ansys Innovation Course
Large deformation
Large deformations can affect load distribution, introducing a nonlinear displacement response.
Notes: Linear and nonlinear FEM – Introduction to nonlinearities and their main sources
In this slide, it is briefly discussed the difference between linear and nonlinear FEM, the main sources of linearities and when to decide what is the best approach to use in a project.
All natural phenomena have some degree of nonlinearity, which can lead to very complex analysis and calculations. In order to simplify some physical problems, especially in solid mechanics field, it is possible to assume a linear comportment of the structures, leading to an approximation that is accurate enough to provide good results.
The underlying equation for structural FEA is a representation of Hooke’s law, where [K] is the global stiffness matrix, {u} is the displacement vector and {F} is the input load vector. This analysis is linear as long as [K] and {F} are not functions of the displacement. With this assumption, it is necessary to consider that the stiffness matrix is a function of only its original shape.
However, in real cases, the stiffness matrix of a structure is deeply related to its geometry, the interactions between surfaces or other components and the material properties. These are the three main sources of nonlinearities in a structural analysis.
Geometry: The change in the shape of the structure can result in change of the wall thickness, the cross-section area and/or the direction of loading. This way, large deformations introduce a nonlinear displacement response.
Contact: It is observed contact nonlinearity when different structures (or difference surfaces of the same structure) have relative motion: either they begin to be in contact, or separate, or slide with friction. This discontinuity in the force-displacement response introduces the nonlinearity.
Material: As all materials have some level of nonlinear behaviour, it is necessary to understand the stress-strain curve of the wanted material. In the elastic region, where the deformations are small, it is possible to consider a linear analysis. However, in the plastic region, where large deformations occur, the nonlinearities have to be taken into account.
To determine which approach is the most indicated, it is necessary to understand what are the main causes of the nonlinear behaviour – if it is one alone or if there is a combination of factors. That understood, it is essential to question if the application allows a simplification in order to avoid huge errors that can be fatal – for example, with biomedical devices, such as helmets and prothesis.
The course “Introduction to Nonlinearities” at Ansys Innovation Space is an interesting bonus to students to understand more about the topics and get some examples.
In the present lecture, only the linear behaviour will be considered, since the introduction of nonlinearities leads to different pre- and post-processing considerations.

## Slide 12: Meshing – Overview
Number of dimensions
1D (Beam elements)
2D (Shell elements)
3D (Solid elements)
Mesh method
Algorithm used by the software to create the mesh
What are the requirements to create a mesh in terms of efficiency and accuracy?
Mesh metrics
The quality of the mesh is defined by mathematical parameters (metrics)
Element shape
Quadrilateral
Triangular
Hexahedral
Tetrahedral
Mesh structure
Structured x Unstructured
How predictable and well defined the location of the nodes are
Element order
Linear (lower order element)
Quadratic (higher order element)
Linear approximation
Actual curve
Quadratic approximation
The Fundamentals of FEA Meshing for Structural Analysis I Ansys Blog
Notes: Meshing – Overview
To create a finite element model, it is necessary to understand the creation of the mesh, which includes various parameters that must be considered.
The first thing is to define the number of the dimensions we’re working with, which leads us to the elements we will use in the project. For a one-dimension simulation, we use beam elements (check previous lecture about 1D elements); for two-dimensional problems, shell elements; and for three-dimensional problems, solid elements. In this lecture, we will focus on 2D and 3D elements, understanding what are the important parameters to consider while creating a finite element model. We will see that it is possible for a model to have a combination of these types of mesh.
With two-dimensional problems, in general, the shape of the elements can be triangular or quadrilateral. In 3D, it is possible to have tetrahedral (tet), hexahedral (hex), pyramidal, prismatic (wedge) and polyhedral shapes, depending on the mesh method. The desirable shape would be the hexahedra, but it can be complex to mesh real-world projects with hex elements. It is suggested to avoid pyramids, but they are also the way to connect meshes that are made of tet and hex elements. We will further discuss the differences of mesh methods and which type of elements they create (check slide 14).
The order of the elements refers to the number of nodes and its respectively displacement response. Linear elements are characterized by a linear shape function, where the displacement response vary linearly with the distance between the nodes. Usually it is less accurate, specially for curved edges, but it does not request a lot of computational power. The quadratic elements, on the other hand, present displacements that must be interpolated using polynomial function. Because quadratic elements provide a more accurate simulation, it tends to be computationally more expensive, taking more time to run the simulation. We will discuss quadratic elements with more details ahead in the presentation (check slide 13) so it is possible to understand how the interpolation works and what are the implications in the variation of displacement and stress distribution.
The mesh structure can be classified in structured and unstructured. The difference between the two of them is the regularity and the organization of the cells. A structured mesh has a regular organization, normally with cells in parallel and uniform space between them. It is also easier and faster to generate structured meshes and it is accurate enough for simple geometries. The unstructured mesh, on the other hand, is not regularly organized and has non uniform spacing between the cells. It has good accuracy for complex geometries, specially for regions with drastic variations, such as sharp corners. However, it is computationally more expensive and not so easy to create, as it needs manual adjustments from the costumer. That said, it is possible to see that both structured and unstructured meshes have their advantages and disadvantages, leading us to analyze what is the best approach for the project we are working in. In this lecture, we will focus in structured meshes.
The mesh method is the algorithm used by the software to create the mesh. There are different methods for solid meshing and for surface meshing and they have to be chosen according to the wanted application, considering geometry complexity and computational power. In this lecture, we will focus on the two main types of meshing methods: tetrahedral element meshing and hexahedral element meshing (check slide 14).
The mesh quality if defined by various mathematical parameters that can define if a result will be enough accurate (good mesh quality) or not (poor mesh quality). There is a list of criteria of mesh metric that can be used to determine the mesh quality – for each of them, there is a spectrum, and the parameter must be in a defined range to be considered as valid. This means the details of the model are well represented and there is mesh independence (check slide 15). Poor mesh quality can lead to convergence difficulties and incorrect physical results. The next slides will discuss what are the metrics used to define the mesh quality (check slide 16).
QUIZ: What are the requirements to create a mesh in terms of efficiency and accuracy?
Answer: It is necessary to create refine mesh in areas with more complex geometry (more details) and a coarse mesh elsewhere. For that, it is important to choose the right mesh method and analyze the pertinent metrics, for the solution accuracy deteriorates as mesh deviates from ideal shape.
As a complementary reading, there is the article “The Fundamentals of FEA Meshing for Structural Analysis”, which discuss briefly how to prepare the geometry for meshing, the types of meshing methods and why is a good mesh important.
Next slide: 5 mesh methods are discussed with a simple geometry (a cylinder) to understand the difference between their generation.

## Slide 13: Meshing – Element Order
Mesh node
A mesh node is a point with specific spatial coordinates, generally located at the vertices of an element. With multiple nodes, it is possible to create a surface (2D) or a solid (3D).
Mid-side node
Some high-order elements have nodes in the mid-points of their edges, but in Ansys default mode they are not shown.
It is possible to control a mesh with mid-side nodes (quadratic or higher order elements) or without mid-side nodes (linear or lower order elements).
Mid-side nodes
Degrees of Freedom
Program Controlled is the default method, which uses linear elements for surface bodies and beam models, but quadratic elements for solid bodies and 2D models.
Linear Element
This option removes mid-side nodes on all elements.
Linear approximation
Actual curve
Lower order elements usually can not represent complex geometries accurately and it is necessary to use a larger number of elements to solve stress gradients.
Quadratic Element
This option keeps the mid-side nodes on the elements.
Quadratic approximation
Although higher order elements represent accurately surfaces and curved edges using fewer elements, it is computationally more expensive.
Notes: Meshing – Element Order
Before talking about what is an element order, it is essential to understand what are the mesh nodes and highlight the possibility of having mid-sides nodes in the mesh. In simple terms, a mesh node is a point with specific spatial coordinates, generally located at the vertices of an element. With multiple nodes, it is possible to create a surface (2D) or a solid (3D) body.
To control a mesh, it is possible to choose low order elements (linear) or higher order elements (quadratic), according to the presence or absence of the mid-side nodes. In a geometry, the less mid-side nodes, the less degrees of freedom.
Physical problems can be expressed by mathematical equations, which can be simple descriptions or complex differential equations. The exact solution can not always be achieved using common analytical methods and it is necessary to use a finite element analysis, which obtains an approximate numerical solution by simplifying the model with discrete locations in the computational domain. Once the equations are obtained considering the physics of the problem (strong form), the weak form defines the shape function.
Linear and quadratic elements are characterized by their shape function. A finite element solver calculates displacements at element’s individual nodes, which are interpolated using different equations. Thus, the solution can be modeled with a linear or a quadratic approximation and can be refined according to the application.
The Linear Element option (lower order) removes mid-side nodes of all elements. It usually can not represent complex geometries accurately and it is necessary to use a larger number of elements (a more refined mesh) to match the analytical solution. It is possible to see a chart with the comparison between the exact solution curve and the linear approximation curve.
The Quadratic Element option (higher order) keeps the mid-side nodes on all elements. It uses a non-linear (quadratic) approximation, as the displacements between the nodes are interpolated using a higher order polynomial. Although higher order elements represent accurately surfaces and curved edges using fewer elements (less refined mesh), it is computationally more expensive – the simulation takes more time to run. It is also less sensitive to element distortion if compared to linear elements.
It is also possible to set the element order as Program Controlled, which is the default option. For surface bodies and beam models, this option uses lower order (linear) elements. For solid bodies and 2D models, it uses higher order (quadratic) elements.
Several parameters can be controlled in the mesh to fit the model’s physics preferences. To affirm the FE model solves accurately the problem, not only the element order is taken into consideration, but also the mesh method and which type of elements is being used. For example, a hexahedral element with linear approximation is more accurate than a tetrahedral element with quadratic approximation. However, lower order tetrahedral elements will make the model stiff and should not be used.
Next slide: We will mention the eight existing mesh methods and discuss five of them: Automatic, Tetrahedrons, Hex Dominant, Sweep and MultiZone.

## Slide 14: Meshing – Mesh Method
This method attempts to combine Sweep and Patch Conforming Tetrahedron if working with a solid model. If it is not possible to use the method, Patch Conforming Tet is used.
Automatic
If the chosen method is Tetrahedrons, it is possible to use two different algorithms: Patch Conforming and Patch Independent. The recommended option for this type of meshing is the Patch Conforming algorithm – which starts meshing from edges, faces and then moves into volume (bottom-up approach).
Tetrahedrons
Hex Dominant
This method creates a mesh made only of hexahedral elements. Generally, it is used for solid models that are not sweepable, since hexahedral elements are preferred to tetrahedral elements.
Sweep
This method generates a mesh with hexahedral and/or wedge elements along the body from a source surface to a target surface (Src/Trg selection), which must be topologically identical. It is not possible to create sweep mesh if the surfaces have interruptions (such as holes and grooves).
Mesh methods available at Ansys
MultiZone
There are three algorithms used in the MultiZone method: Standard, Thin Sweep and Cart Sweep. The default algorithm (Standard) generates hex dominant meshes by surface and volume block decomposition into mappable and sweepable volumes.
Notes: Mesh Methods
There are 8 different types of mesh methods on Ansys Workbench platform. In this slides, we will discuss briefly 5 of them, trying to comprehend what is better for the chosen geometry and application.
The Automatic method attempts to combine Sweep and Patch Conforming Tetrahedron while working with a 3D model. If the body is not sweepable, only the Patch Conforming Tetrahedron method is used. It is possible to check if the body is sweepable or not by right clicking on mesh cell in the tree on “Show Sweepable Bodies”.
The Tetrahedrons method generates a mesh composed by tetrahedral elements. It is possible to choose between two different algorithms: Patch Conforming and Patch Independent. The Patch Conforming algorithm is the recommended option for tetrahedral meshing, following a bottom-up approach – it generates the mesh first on the edges, then faces, then volumes. It is possible to use local defeature sizes for more control of the mesh. To guarantee that the mesh is robust, it is necessary to confirm if the mesh face size is smaller than the geometric faces – the default defeature size is set to ½ of the minimum size. The Patch Independent method does not have any advantages and it is considerably slower – it is only worth trying if there is some corruption in the body’s geometry.
The Hex Dominant method generates a mesh made only of hexahedral elements. It is recommended for bodies thar are non-sweepable, instead of choosing tetrahedral methods.
The Sweep method generates a mesh with hexahedral and/or wedge elements along the body from a chosen source surface to a target surface. It is necessary that the source and the target surfaces are topologically identical so the mesh can be generated. If the cross section of the body has any interruptions (such as holes or grooves along the length), it is not possible to create the sweep mesh. It is also possible to choose if the Source/Target selection will be either automatic or manually. In automatic selection, the algorithm already determines the best source and target for the body. If we choose to do it manually, it is possible to choose just a source (and the algorithm chooses the best target) or both (source and target). We also can choose how many divisions we want to create along the sweep path, which impacts the way the mesh in structured.
When using MultiZone method it is possible to choose between three different algorithms: Standard, Thin Sweep and Cart Sweep. The default MZ algorithm (Standard) generates automatic hex dominant meshes by surface and volume block decomposition into mappable and sweepable volumes. It is possible to detect blocks with bad angles and automatically cut them to create a better orthogonal mesh. The Thin Sweep creates a 2D blocking and pulls across a thin body to form a 3D mesh (recommended for thin bodies). Finally, the Cart Sweep algorithm uses a cartesian background grid to create an automatic blocking.
Next slide: We will discuss the concept of convergence study through mesh refinement and when a mesh is considered independent. We will see that mesh independence is one of the factors for a good mesh, but not the only one. Good geometric representation, analysis of mesh metrics and the process of mesh refinement are also crucial for an efficient and accurate model.

## Slide 15: Meshing – Mesh Independence & Convergence
A mesh is independent…
…when it is possible to obtain the converged solution after which mesh refinement does not change the result anymore.
Geometric representation
All the geometric details are well captured
Mesh Independence
The mesh doesn’t alter the solution (convergence study)
Mesh Metrics
The quality criteria are within a correct range
Mesh Refinement
Coarse or fine mesh depending on the complexity
Good
Mesh
What is convergence?
The process of convergence consists in decreasing the element size and analyzing its impact in the solution of the underlying partial differential equations.
Smaller mesh size
More accurate solution
Larger simulations
Longer runtimes
Optimal balance
Refine the mesh in the area of interest by changing the mesh size and maintaining element type and order.
Choose a result to study, such as stress values, plastic strain, fatigue life, etc.
Compare the results for the various runs and plot a convergence curve in a chart number of nodes vs stress values, for example.
Element Size
0.005m
Element Size
0.003m
Notes: Meshing – Convergence study and Mesh Independence
To define if we have a good or a bad mesh for our model, it is essential to check some steps, such as:
A good mesh captures the geometric details well (such as curves, holes and small details).
The mesh doesn’t alter the solution, i.e. the mesh is independent.
Some quality criteria are within a correct range (study of mesh metrics).
The model doesn’t have to be refined at its maximum: A good mesh is coarse where it can be coarse and fine when it needs some refinement. This maintains the good accuracy of the model, but it also does not increase the runtime, which is computationally and financially more efficient.
With these criteria respected, it is possible to have a good mesh to run the simulation and achieve physically realistic results.
But what does “convergence” mean and how do we conduct this study?
The process of convergence consists in decreasing the element size and analyzing its impact in the solution of the underlying partial different equations of the model.
In general, the smaller the mesh size, the more accurate the solution is. However, this can lead to larger simulations, with a lot of data to store and longer calculation times. Thus, it is important to run convergence studies to find an optimal balance between the model accuracy and the runtimes.
Finally, a mesh is considered as independent when…
It is possible to obtain the converged solution after which mesh refinement does not change the result anymore.
However, before starting the convergence process, it is essential to check if we have a clear understanding of the physics of the problem (e.g. geometry, boundary conditions and material properties).
Once it is all set and the mesh if finally created, we choose an area of interest (it can be just a specific part of the model or the whole geometry) and we refine its mesh but changing just the mesh size and maintaining element type and order, which assure a fair comparison between the simulations we will run.
We must choose a result to analyze, e.g. stress values, plastic strain or fatigue life, depending on what is interesting for the application.
After running at least 3 simulations, it is possible to plot the convergence curve. In the chart stress vs number of nodes, it is possible to observe a point when the increase of nodes does not impact significantly the stress results.
It is shown in this slide a convergence curve with Equivalent von Mises Stress (Y-axis) and the number of mesh nodes (X-axis). This example is part of the analysis of the wrench model which we will discuss on slide 46, after the section of 3D elements.
Next slide: We will introduce the importance of a good mesh quality and the features in the Ansys Mechanical software that can be used to check it, such as mesh statistics (minimum, maximum and average sizes of elements with its standard deviation) and metric graphs.

## Slide 16: Meshing – Mesh Quality
What is the impact of mesh quality on the solution?
Mesh Quality Worksheet
Each type of analysis has its different mesh requirements, which means there isn’t a perfect formula to determine whether the FE project has a good mesh quality. It is essential to understand the physics of the model and its particularities, making sure there is not convergence issues or high calculation times.
Metric Graph
Some factors may affect the quality of the mesh, such as geometry problems, incorrect meshing parameters and/or not appropriate meshing methods.
Notes: Mesh Quality – Statistics, Graph and Mesh Quality Worksheet
There are some ways to verify if the generated mesh is acceptable for the model or not. One of these is to conduct a mesh independence study, as we saw in the previous slide. However, it can take a significant amount of time. To access mesh statistics during and after the mesh generation, there are some tools that can be used.
First, it is necessary to choose a mesh metric – each one is calculated a different way and has its own scale of what is a good or a bad element. We will discuss some of these metrics in the next slide.
Once the mesh metric is chosen, it is possible to check its statistics. The example in the slide shows the statistics for the Element Quality metric, which displays not only the minimum and maximum element sizes, but also the average element size and the standard deviation. Different metrics will display different values for each statistic.
It is also possible to check the number of nodes and elements that were created in the mesh.
In Check Mesh Quality section, it is possible to activate the automatic shape checking. One may choose between displaying “error and warnings”, just “errors” or to create the Mesh Quality Worksheet. If any of them is set, the algorithm will show the elements that do not fit with the physical requirements of the model (specific error limits). Each quality criteria has its own limits for each type of analysis, which lead the understanding of what is a good mesh to a particular comprehension of the project.
  The Mesh Quality Worksheet is a table of Physics Preference, which is based in the criteria for shell and solid elements. If any “Error Check” box is enabled, the mesh will be invalidated if failure limits are exceeded in this specific metric – This approach is recommended when the mesh must follow strict standards. The column “Worst” shows the worst metric for the criteria and highlights by color if it is in a “good” (green), “warning” (yellow) or “failure” (red) state.
For the chosen mesh metric, it is created a metric graph, a histogram where it is possible the element quality distribution – which can be by the number of elements with specific statistics or by the percentage of volume/area. The example in the slide shows that most of the elements have a good element quality (metric closer to 1). If the model has more than one type of element, it be shown in the histogram with bars of different colors. It is possible to control this graph by selecting the types of elements you want to plot, as well as the range on the axis and the number of the bars.
However, it is possible to highlight the reasons why the mesh has its quality affected. It can be a geometric problem, i.e. the model may have smalls edges, sharp angles and/or gaps. The mesh parameters can be incorrect, for example, the model may present large minimum size. Also, the meshing method may not be the most appropriated for the application – Hex dominant meshes, for example, can result in pyramidal elements, which lower the quality of the mesh. Once it is noticed the reasons of the poor mesh quality, it is possible to make the right changes and refine it just the necessary to make the mesh suitable for the project.
It is essential to mention that there is no absolute truth of what is a good mesh quality, since different types of analysis have their own mesh requirements, which must be studied to fit the particularities of the physical model. However, one should pay attention to have a mesh neither with convergence issues nor high calculation times.
Quiz: What is the impact of mesh quality on the solution?
The solution of a finite element simulation has strict dependency of the mesh quality, once it has impact on project’s accuracy and computational efficiency. In terms of accuracy, a good quality mesh captures the details of the geometric, using elements that are close to an ideal shape as possible. High quality meshes do not need a lot of elements to achieve accurate results – the higher the number of elements, the higher the computational costs in terms of memory and calculation time. Poor mesh quality can also result in convergence difficulties or a bad description of the physics, leading to a wrong conclusion, specially when the model has more complex features, such as material nonlinearities, large deformations or parts in contact. In summary, a good mesh quality gives reliability, prediction robust solutions.
Next slide: We will discuss in detail four of the mesh quality criteria (Element Quality, Aspect Ratio, Jacobian Ration and Skewness).

## Slide 17: Meshing – Mesh Metrics
Element Quality
This metric varies from 0 (worst) to 1 (best), where 0 indicates the element has a zero area/volume and 1 represents a perfect square (2D) or cube (3D).
For 2D quad/tri elements:
For 3D brick elements:
0 (worst)
1 (best)
Aspect Ratio
This metric ranges from 1 (best) to ∞ (worst).
In 2D models, it represents the length to height ratio .
In 3D models, it represents the area ratio or the radius ratio of circumscribed/inscribed circle.
1
20
Skewness
This metric ranges from 0 (best) to 1 (worst) and determines how close to ideal (equilateral or equiangular) a face or cell is.
Equilateral volume deviation:
Normalized angle deviation:
Applied only for triangles and tetrahedrons
good
Highly skewed
Bad
Expected
Fail
Jacobian Ratio
This metric ranges from 1 (best) to ∞ (worst), but really bad values can appear as .
It is based on the determinant of the Jacobian matrix by comparing the shape of a given element with an ideal one.
Quadrilateral
Rectangular
Bad
Expected
Fail
Notes: Mesh Metrics
The results of a numerical simulation are dependent on the quality of the mesh. To assure the mesh has good quality, there are some criteria to analyze which can be quantified in various ways. In this slide, we will discuss four of these criteria (or metrics): Element Quality, Aspect Ratio, Jacobian Ratio and Skewness.
The Element Quality metric varies from 0 (worst) to 1 (best), where 0 indicates that the element has a zero area/volume while 1 represents a perfect square (in 2D case) or cube (3D). To calculate this metric, it is necessary to take in consideration the ratio of the volume to the edge length for a given element. In the slide, it is possible to check the equation for 2D and 3D cases. This mesh metric is one of the most used for structural analysis.
The Aspect Ratio metric varies from 1 (best) to infinite (worst). It is possible to determine the aspect ratio for triangles, quadrilaterals (2D) and tetrahedrons (3D). For 2D models, it represents to length to height ration. For example, for triangles, a value of 1 indicates an equilateral triangle; for quadrilaterals, it indicates a square. In 3D models, it represents the area ratio or the radius ratio of circumscribed/inscribed circle. This metric is also very important for structural analysis.
  In the slide, it is possible to see a representation of a good element (triangle with aspect ratio equal to 1) and a bad element (triangle with aspect ratio equal to 20).
The Jacobian Ratio metric ranges from 1 (best) to infinite (worst), but really bad values can appear as -100. It measures the shape of a given element compared to an ideal element based on the determinant of the Jacobian matrix. In this slides, it is possible to check good, bad and failed quadrilateral and rectangular elements under the perspective of the Jacobian Ratio metrics. A good quality mesh presents the Jacobian Ratio between 1 and 10 for the majority of its elements.
Finally, the Skewness metric is one of the most important mesh metrics to study, since it determines how close to ideal (equilateral or equiangular) a face or cell is. It varies from 0 (best) to 1 (worst) and can be calculated by two different methods: equilateral volume deviation and normalized angle deviation. The first one is applied only for triangles and tetrahedrons and its equation is the ration of the difference between the actual and the ideal cell size to the ideal cell size. However, the normalized angle deviation can be applied to all cell and face shapes, but it is frequently used for hexa, prisms and pyramids. In the slide, it is possible to see Ɵmax (maximum angle in the cell), Ɵmin (minimum angle in the cell) and Ɵe (equiangular face/shell angle, which is 60° for tets and 90° for quads and hexas).
  In the slide, it is possible to check the difference a good element (equilateral triangle) and a highly skewed element.
Next slide: We will discuss two discretization approaches in finite element analysis that are used to refine the mesh, i.e. increase the solution accuracy. The first approach, h-refinement, refers to the element’s length, while the second one, p-refinement, refers to the order of the polynomial order.

## Slide 18: Meshing – Refinement
In pursuit of increasing the solution accuracy and ensuring numerical convergence, two discretization approaches can be adopted:
Original Mesh
2 x 4-noded quadrilateral elements
8 x 4-noded quadrilateral elements
h-refinement
Increased number of elements
p-refinement
2 x 8-noded quadrilateral elements
Increased order of the shape functions
Number of elements (/)
Young’s Modulus (GPa)
p-refinement
h-refinement
actual stiffness
Notes: Meshing – Refinement
There are different discretization approaches to refine the mesh of a FE model, i.e. to increase the accuracy of the solution and ensure the numerical convergence.
The h-refinement refers to the characteristic length of the elements, where the variable “h” is used to specify the step size in numeric integration. By reducing the “h” parameter, this method increases the number of elements in the mesh. For a coarse mesh, with few elements, the stress distribution deviates significantly from the analytical results, sometimes leading to stress jumps, for example. It is necessary to run the simulation several times with finer meshes until the results don’t have significant changes from one simulation to another (achieve numerical convergence).
The p-refinement refers to the order of the shape functions, which are increased to improve the accuracy of the solution. The letter “p” stands for polynomial and, as it was seen on slide 13, the higher the order of the elements, the more accurate the solution is. However, differently from the h-refinement, this method does not need to change the mesh. To this refinement, the first solution must be run with a first order polynomial shape function. The next solutions may use second or third order polynomial shape function. Again, the model does not need to be refined anymore when the results do not have significant changes from two runs.
Next slide: We will discuss sizing controls to provide finer meshes at regions that can be problematic to the solution, e.g. curved areas and details. The size functions to be discussed are adaptative, curvature, proximity and a combination of curvature and proximity.

## Slide 19: Meshing – Sizing Control
The sizing control ensure greater control over the mesh growth between small and large element sizes, the curvature-based refinement and the number of the elements in the gaps between two geometries (proximity-based sizing). The controls for sizing include Element Sizing, Growth Rate, Maximum Size, Curvature Minimum Size and Proximity Minimum Size.
Curvature
It refines meshes at curve edges and faces, ensuring the element size does not violate the maximum size or the curvature normal angle.
Proximity
Refinement is based on the minimum number of element layers created in regions with “gaps” between geometric entities.
Numerically Accurate Results I Ansys Innovation Course
Adaptive
By default, the adaptive sizing is set. In this method, there is no automated refinement on curvature or proximity regions.
Curvature & Proximity
Combines curvature and proximity methods.
Notes: Meshing – Sizing Control
The Sizing Options provide control over the mesh growth (between small and large sizes), curvature-based refinement (curvature-based sizing) and the number of mesh elements between two geometric entities (proximity-based sizing). Controls for sizing include Element Size, Growth Rate, Maximum Size and Curvature Minimum Size / Proximity Minimum Size. For example, the Element Size is the global maximum size of the elements.
In the menu, Use Adaptive Sizing is set to Yes. In this method, there is no automated refinement on curvature or proximity regions. In the first picture, it is possible to check the generated mesh of a dog-bone sample with a hole when the Adaptive Sizing is set to Yes.
If Use Adaptive Sizing is set to No, there are three possibilities: 1) choose just a curvature-based sizing; 2) choose just a proximity-based sizing; 3) choose to combine curvature and proximity methods.
If Curvature is set to Yes, the mesher examines curvature on edges and faces, so the current size does not violate the maximum size or the curvature normal angle, which is the maximum allowable angle for an element edge.
If Proximity is set to Yes, the refinement is based on the minimum number of element layers created in regions with “gaps” between geometric entities. A “gap” can be defined as the internal volume between two faces or the area between two opposing edges of a face.
If both Curvature and Proximity are set to Yes, the two mentioned analysis are considered in the mesh generation. In the second picture, it is possible to see the same dog-bone specimen when the Curvate & Proximity method is set to Yes.
In the following slides, we will work with this dog-bone specimen in a task to manipulate the quality of the mesh, testing different mesh methods, element orders and sizing controls.
Next slide: We will discuss about the Solver of the Ansys Mechanical tool and the process of getting the results of Deformation and Stress. A difference between Stress Concentration and Stress Singularity will be clarified.

## Slide 20: Solver – Deformation and Stress
u
ɛ, σ
Governing equations
Calculate displacement (u) on the nodes
Calculate strain ɛ on the integration points
Calculate stresses σ from the strains
Stress singularities
Stress concentration
A stress singularity is a point where there is no convergence of stresses values, usually tending to infinite.
Stress concentrations, on the other hand, are points where stress concentrates, but the values still converge.
The presence of stress singularities does not necessarily mean wrong results, once singularities are local affects. Nearby displacements and stresses should be correct.
Topics in Structural Simulation in Ansys Mechanical I Ansys Innovation Course
Some simplifications in FE models can cause stress singularities. It is possible to mention the presence of sharp corners in the geometry, the application of point loads/restraints at a single node or the assumption of a linear-elastic model when under large deformations.
With sharp corners
With round corners
Notes: Solver – Deformation and Stress
In this slide, we will discuss the steps to obtain deformation and stress using the Ansys solver.
In the simulation, the displacement DOFs are solved on the nodes, but the stresses and strains are calculated on the integration points. After considering the governing equation, as saw in the slide 8 and 10, the first step is the calculation of the displacements on the nodes. The second step is the calculation of the strains on the integration points, where B is the matrix that denotes normal and shear components (strain-displacement matrix). Finally, the stresses are calculated from the strains.
FE models are simplifications of the actual project, leading to an approximate result of the exact solution. Some possible simplifications may include sharp corners in the geometry, the application of point loads/restraints at a single node and the assumption of a linear-elastic regime when it is not recommended – e.g. under large deformations.
These simplifications can cause a divergence in the stress values with the mesh refinement. The regions where the stresses do not converge are called stress singularities. One must not mistake stress singularity with stress concentration, which are regions where the stress concentrates, but still converges to finite values.
However, stress singularities do not necessarily indicate an invalid FE model, since they are local affects. This means that nearby displacements and stresses should be correct, even though they do not reflect the actual stress at specific points. Sometimes, it is not practical or even possible to remove all singularities, so in this case one of the recommended actions is to use the critical engineering judgement.
In this slide, it is possible to check a simple example of a dog bone model and the difference between the equivalent von Mises stresses between the geometry with round corners (on the left) and with sharp corner (on the right). Both models have the same load and support conditions – fixed support at one end and a distributed force at the other end. The mesh metrics are the same. However, the model with sharp corners presents stress concentrations in the regions around these corners and it is more likable to present stress singularities. The values of minimum, maximum and average stress are displayed just below the images.
To learn more about stress singularities and solving structural simulations using the Ansys Mechanical software, a resource on Ansys Innovation Space is disponible as “Topics in Structural Simulation in Ansys Mechanical”.
Next slide: We will follow an exercise with a dog bone specimen to understand how the mesh methods, the element order and the sizing controls (such as size functions and element size) influence the mesh quality.

## Slide 21: Task – Dog Bone Specimen
Consider this dog bone specimen for a tensile strength test [1]. The goal is to change the element order, the meshing methods and the sizing controls to check how they affect the mesh metrics. Start with an Automatic mesh and Element Size equals to 2.5mm. Among the different mesh metrics, in this exercise it will be analyzed the Element Quality.
[1] ISO 527‑1:2019, Plastics — Determination of tensile properties – Part 1: General principles.
Note: The CAD file is attached: dogbonespecimen.scdoc
150 mm
150 mm
20 mm
10 mm
80 mm
R20 mm
Notes: Task – Dog bone specimen – Problem Statement
This slide shows the problem statement of a dog bone specimen simulation. Dog bone samples are used in tensile strength tests to evaluate the mechanical properties of materials, like metals, polymers or composites.
The geometry is based in ISO 16630, a primary standard used to describe the hole tension test and its constraints. This test is important to understand how the materials behaves under tensile stress when it has a discontinuity, which can act as a stress concentrator.
The dimensions are written in the slide to be reproduced if wanted. The file is also available for download. The goal is to change some parameters, as the element order, the meshing methods and the sizing controls (such as the sizing functions and the element size) to analyze how the mesh metrics vary. The chosen mesh metric was Element Quality, which is commonly used in static structural simulations. However, the student can explore the other mesh metrics with the theory presented on slide 17.
The exercise starts with an Automatic mesh and Element Size equals to 2.5mm. The mesh method and the element size will be changed in the next slides.
Next slide: After setting the automatic mesh method and the element size, it is possible to see the mesh statistics (minimum, maximum and average element quality, as well as the standard deviation) and the mesh graphs with the respective element types.

## Slide 22: Dog Bone Specimen – Mesh Method
1
Set the mesh to Automatic and Element Size to 2.5mm.
0 (worst)
1 (best)
Element Quality Metric
Click on one of the bars in the histogram to display the elements of a specific type and metric.
Notes: Task – Dog bone specimen – Automatic Mesh Method
In this slide, it is possible to observe the created mesh when one chooses the automatic mesh method with the element size equals to 2.5mm.
As discussed in the slide 17, the Element Quality metric rates from 0 (worst) to 1 (best). With the automatic mesh method, the statistics show an average element quality of 0.94845, which is a good value for this metric. There is low standard deviation among the quality of elements.
With the mesh graphs, it is possible to analyze the existing element types in the mesh and their distribution according to the mesh metrics. In this case, there are two element types: HEX20 and WED15, but HEX20 represents almost all the elements of the mesh. By clicking on one of the bars of the histograms, the Ansys Mechanical software will display the respective elements with this specific quality.
  HEX20 represents a 20-node hexagonal element, while WED15 is a wedge shape element with 15 nodes. Both are high order (nonlinear/quadratic) elements. The WED15 elements are generated by the condensation of HEX20 elements. To remember what are the element orders, come back to slide 13.
  Because of their shape, WED15 elements are not desirable in the mesh, so if there is a considerable number of these elements, the recommendation is to check if they are present in critical areas and, if yes, re-mesh the model.
Next slide: We will maintain the element size as 2.5mm, but the mesh method will be changed to Hex Dominant. The same analysis of mesh statistics and mesh graph will be made.

## Slide 23: Dog Bone Specimen – Mesh Method
Insert Hex Dominant as the mesh method and update the model.
2
There is the creation of pyramidal elements, which are more likely to suffer element distortion in analysis.
It is possible to observe the average Element Quality decreased in comparison to the Automatic method.
Notes: Task – Dog bone specimen – Hex Dominant Mesh Method
The second step is to change the mesh method. We will insert a Hex Dominant method and re-generate the mesh with the same element size. This method is usually recommended for bodies which can not be swept.
It is possible to observer that, although there are elements with the maximum element quality (0.99955), the average is 0.69268, lower than the average of the automatic mesh method that we analyzed before. Also, there is significant standard deviation. Opening the Mesh Graph, it shows that there are 4 types of elements: TET10, HEX20, WED15 and PYR13.
  TET10 is a 10-node tetrahedral quadratic element, while PYR13 is a pyramidal element with 13 nodes.
Although the most of elements are HEX20, the presence of a significative number of PYR13 elements turns this method as a worse alternative if compared to the automatic mesh method and should not be chosen to further analysis according to this mesh metric.
Next slide: The third and last mesh method will be the Tetrahedrons. Similar analysis will be conducted.

## Slide 24: Dog Bone Specimen – Mesh Method
Insert Tetrahedrons as the mesh method and update the model.
3
Although there are only tetrahedral elements, the standard deviation between the metrics is still greater than the automatic mesh.
It is possible to observe the average Element Quality decreased in comparison to the Automatic method.
Notes: Task – Dog bone specimen –Tetrahedrons Mesh Method
The third and last method to be analyzed is the Tetrahedrons, which algorithm was set by default as Patch Conforming. This is a bottom-up approach, where the meshing process starts from the edges, faces and then the volume, well capturing the geometry details. To remember the characteristics of Patch Conforming Method, come back to slide 14.
The average element quality is 0.69403, which is slightly higher than the average element quality with Hex Dominant method. Also, the standard deviation is lower, but still greater than the automatic mesh conditions. The only element type that is present in this mesh in TET10.
Among these 3 options, the automatic mesh method gives the best metrics and, consequently, a more accurate analysis. It is important to add that even with simple geometries like this specimen, choosing meshes with PYR13 and WED15 in critical areas can lead to less accurate results when running the simulation. Because of that, the Automatic mesh will be the chosen method to follow the analysis.
Next slide: The second part of the analysis is the element order. It will be shown the differences between the default (Program Controlled), linear (low order elements) and quadratic (high order elements).

## Slide 25: Dog Bone Specimen – Element Order
Set the mesh to Automatic again. In the Defaults group, change the Element Order. The default is Program Controlled.
Program Controlled
Linear
Quadratic
*No mid-side nodes.
Notes: Task – Dog bone specimen – Element Order
The second part of the analysis is to change the element order to understand how it affects the element quality. The generated mesh remains with 2.5mm as the element size and the method is set to Automatic. By default, the chosen Element Order is Program Controlled. To remember the differences between the three categories of element order, come back to slide 13.
After choosing the element order, it is possible to analyze detailed statistics, which show not only the number of nodes and element, but also the number of mid-side nodes and how many are the elements of each type.
In the Program Controlled option, since we are working with a solid body, it will generate high order (quadratic) elements. It is possible to see that this option is identical to the quadratic one. The Linear option shows a lower number of nodes and no mid-side nodes.
*Note: Both linear and quadratic elements are supported for 2D shell models.
Next slide: The third and last part of the analysis are the sizing controls. We will discuss about sizing functions (adaptive, curvature and proximity) and the impact in the mesh metrics when changing the element size.

## Slide 26: Dog Bone Specimen – Sizing Controls
By setting Adaptive Sizing to Yes or No, the mesh distribution along the geometry changes.
Curvature & Proximity
Adaptive
vs
Notes: Task – Dog bone specimen – Sizing Controls
The last part of this analysis is divided in two different approaches: changing the sizing functions and varying the element size. To remember the basic concepts of sizing functions, come back to the slide 19.
SIZING FUNCTIONS:
There are several typer of sizing options (e.g. resolution, growth rate, curvature and/or proximity size) and its relevance depends on the sizing controls that is being used. The three sizing functions are adaptive, curvature and proximity, but it is also possible to combine curvature and proximity options. The default method in the Ansys Mechanical tool is setting Adaptive to Yes.
  While using the adaptive sizing, it is possible to define the resolution, which controls the mesh distribution. The range of values is 0 to 7, with the mesh resolution changing from coarse (zero) to fine (seven).
  Another option that can be controlled is the transition, which affects the rate at which adjacent elements will grow. It can be set to slow (smooth transitions) or fast (abrupt transitions).
  The Span Angle Center is an option dedicated for curvature-based refinement, i.e. for a curved region, the mesh will subdivide along the curvature until the individual elements span this angle. A coarse mesh around curved areas presents Span Angle between -91° and 60°, while a fine mesh ranges from -36° to 12°.
If the Adaptive Sizing is set to No, there are three different possible approaches: 1) Set only Capture Curvature to Yes; 2) Set only Capture Proximity to Yes; 3) Set both Curvature and Proximity to Yes.
When Capture Curvature is set to Yes, it is possible to define 2 different parameters: Curvature Min Size and Curvature Normal Angle.
  The Curvature Min Size is the minimum element size that is returned to the mesher. If one changes the Element Size, the Curvature Min Size is recalculated.
  The Curvature Normal Angle is the maximum allowable angle that one element edge is allowed to span given a particular curved region. It is possible to set a value from 0 to 180° or even accept the default – which depends on the type of analysis that is being considered.
When Capture Proximity is set to Yes, it is also possible to define 2 parameters: Proximity Min Size and Proximity Gap Factor.
  The Proximity Min Size allows the specification of a minimum size to be used in proximity sizing calculations. By default, it is equal to the Curvature Min Size.
  The Proximity Gap Factor is the minimum number of layers of elements that are created in the gaps. It is possible to choose a value between 0 and 100, but the default is 3. It is important to highlight that this is an estimated value and may not be the same in every gap.
On the bottom of this slide, there is a link for the Ansys documentation about the sizing options.
Next slide: Besides the mesh size controls the element size plays another important role for the mesh quality.

## Slide 27: Dog Bone Specimen – Element Size vs Element Quality
Element Size vs Element Quality
In general, by increasing the element size, the average element quality decreases. Some meshes with certain element sizes can introduce wedge and pyramidal elements, which can decrease the mesh quality.
Notes: Task – Dog bone specimen – Element Size vs Element Quality
ELEMENT SIZE vs ELEMENT QUALITY:
Another sizing control is to change the element size and check how it affects the mesh metric. In the graph on the right side of the slide, one can observe how the average element quality decreases when the element size gets greater.
The table on the left displays the associated parametric study set up for the Ansys Mechanical software.
 In general, by increasing the element size, the average element quality decreases. Some meshes with certain element sizes can introduce wedge and pyramidal elements, which can decrease the mesh quality.
Next slide: Now that we had an overview about how to analyze the quality of the generated mesh, we will discuss, with more details, the differences between 2D (plane) and 3D (solid) elements.

## Slide 28: Meshing – Discretization in 1D, 2D and 3D Elements
1D Elements
2D Elements
3D Elements
Examples
Beam/truss
Spring
Element Representation
FEA Representation
Truss Structure
Examples
Plate
Sheet
Element Representation
FEA Representation
Soda Can
Examples
Bracket
Table
Element Representation
FEA Representation
Cube
…
…
simplify
apply
simplify
apply
simplify
apply
L
V
A
Shell
Membrane
Beam
Truss
Hexahedrons
Tetrahedrons
Pentahedrons
…
…
Lecture Unit: Introduction to Finite Element Analysis (1D Elements) with Ansys Mechanical
Notes: Discretization – 1D, 2D and 3D elements
Depending on the geometry and its complexity as well as the desired (re)solution accuracy (degrees of freedom) and computational time, one must choose between 1D, 2D and 3D elements.
(*Click*)
1D (Line) Elements
In this lecture unit, the focus lies on 2D and 3D elements. For further reading/information on the use of 1D elements in FEA, please refer to the lecture unit linked here.
2D (Plane) Elements
Some examples for geometries that lend themselves to be represented by 2D elements are plates and sheets as well as thin-walled geometries like cans (see slide).
Typical 2D elements used to represent these type of structures are shells and membranes.
FEA representation: Soda Can.
3D (Solid) Elements
All geometries can be represented by solid 3D elements, however, for simple geometries like beams it might be more computationally efficient to use 1D elements. Likewise, a use of 3D elements for structures with a large ratio between length/width to the thickness (plate-like structures), a large number of elements would be required to ensure sufficient number of elements through the thickness. Thus, 3D elements might not be favorable in regard to the computational effort required. Some examples that lend themselves for the use of solid elements are shown here (bracket and table).
There is an abundance of elements that can be employed, which are usually characterized by tetrahedral or brick shapes.
FEA representation: Cube.
Next slide: We will discuss the differences between shell and solid elements.

## Slide 29: 2D Area vs 3D Volume Elements – Overview
2D Elements
A
The 2D elements are characterized by triangular or quadrilateral shapes.
The 3D elements are characterized by tetrahedral or brick shapes.
The choice of elements is dependent – among others – on:
  DoF: Displacements/rotations in 2D or 3D space
  Material properties: Linear vs non-linear (e.g. plasticity)
  Deflection/strain magnitude: e.g. geometric non-linearity due to large deformation/rotation
  (Re-)solution accuracy: Elements with larger number of nodes will yield higher solution accuracy (i.e. p-refinement)
  The DoF of an element also determines which disciplines can be modelled, i.e. structural mechanics, thermal analysis, fluid mechanics, electromechanics, etc.
  One generally aims at running computationally efficient simulations; thus, elements should only have the required DoF and features.
3D Elements
vs
V
Notes: Discretization – 1D, 2D and 3D elements
1D (Line) Elements
Typical examples for 3D structures which can be simplified into 1D elements in FEA are beams and trusses as well as springs. The corresponding 1D elements are likewise called beams, bars, truss, rod or links.
(*Click*)
Consequently, structures made of such constituents can be modeled using 1D elements, however one must also choose the type of analysis (2D vs 3D) and the DoF necessary to resolve the problem at hand (see next slide). This is linked to the type of element.
The choice of elements is dependent – among others – on:
  DoF: Displacements/rotations in 2D or 3D space
  [Beam elements/theory: Timoshenko vs Euler-Bernoulli theory based on slenderness ratio]
  Material properties: Linear vs non-linear (e.g. plasticity). For non-linear material properties or large strain magnitudes, the aforementioned linear relation between the stiffness, the force and the displacement is not linear for large deformations.
  Deflection/strain magnitude: e.g. geometric non-linearity due to large deformation/rotation
  (Re-)solution accuracy: Elements with larger node number will yield higher solution accuracy (i.e. p-refinement). This in turn will increases the solution memory requirements.
  The DoF of an element also determines which disciplines can be modelled, i.e. structural mechanics, thermal analysis, fluid mechanics, electromechanics, etc.
  One generally aims at running computationally efficient simulations; thus, elements should only have the required DoF and features.
  In the simulation with 1D elements, lines and curves are meshed, which is simple, as only the position and shape rather than the volume is considered. Each line element is associated with the cross-section of the actual structure.
Note: A single node would be considered a point element and can for instance be used a mass element.
Further reading: Please see the documentation for the Ansys Mechanical software to find out more on the different element types available, including the DoF, applicable physics, etc.

## Slide 30: Degrees of Freedom – Overview
1D space: Line
A
B
x
The nodes can move along the line, but not vertically.
2D space: Plane
F
A
B
F
x
y
The nodes can move along and rotate around the X and Y axes.
3D space: Box
Degrees of Freedom (DoFs) can be defined as the possibility to move in a defined direction in space.
x
y
z
Degrees of Freedom
Dimension of the elements
2D Elements
3D Elements
A*
B*
1 Translation
0 Rotations
1 Internal Force
2 Translation
1 Rotation
3 Internal Forces
3 Translation
3 Rotations
6 Internal Forces
A
B
A*
B*
The nodes can move along and rotate around the X, Y and Z axes.
Notes: Discretization – 1D, 2D and 3D elements
Firstly, it is important to understand that the analyses with 2D and 3D elements are directly related to the Degrees of Freedom (DoFs) of the nodes of the finite elements. Likewise, the nodal DoFs tightly connected to the model dimensions, i.e. translation or rotation in a 1D, 2D or 3D space.
Spaces with 1 dimension are generally used when we’re working with Finite Element Analysis by hand. Because it has just 1 dimension, the nodes can only move along a line, either from A to B or from B to A (i.e. they cannot deviate from the path which is defined by the line/string). In an applied engineering case, in a 1D space, the forces also can only act along the line. We can consider tension or compression, but to model a bending beam, it would be necessary to have another dimension. To go further on 1D models, please check the previous lecture unit, where the theory of one-dimension problems are detailed.
In a 2D space, each node carries 3 DoFs: movement along axis X, movement along axis Y and rotation “in plane”. To solve this type of problem, once now it is possible to translate and rotate in the plane, it is necessary to set the right boundary conditions (loads and supports) to avoid possible non-convergence problems. However, in 2D cases, not only the possibility of movement is considered, but also the internal forces that act in the model – we can mention the normal forces (since it acts normal to the cross-section surface), the shear forces and the in-plane bending.
The elements in this case can be tension or compression along x and/or y and in shear, meaning the 3 DoFs lead to 3 stress components, for example.
In 3D space (with 3 dimensions) there 6 possible movement for each node: not only the movement along X, Y and Z axes, but also the rotation around them. Once the model can rotate around its own axis, we also start talking about torsional moment.
However, we can mention that the number of possible stresses in 3D does not need to be equal to the number of DoFs. Differently from the 2D space, where the elements have no thickness, in 3D space the stress distribution through thickness is considered – later, we will discuss about the application of thick and thin-walled structures and how to choose the right elements for their analysis. Besides the stress components in 2D space, it is also important to mention the bending around X and Y axes, the out-of-plane shear components and the torsion.
At this point, it is crucial to understand that once can also choose the dimension of the elements – i.e. there are 2D and 3D elements. What can be confusing for those who are starting with FEA studies is that analysis in a three-dimensional space can happen either with 2D or 3D elements.
In this context, 2D elements can be used in 2D or 3D analysis. The 2D elements in a 2D analysis are called surface elements; in a 3D analysis, they are shell elements.
However, when we talk about 3D elements (solid elements) in a 3D space, there are not 6 DoFs anymore, but 3 in each node. This happens because the rotation is no longer considered, once it is possible to consider bending as a difference in normal stress in any direction – the elements are connected by the so-called pinned connection.
Next slide: We will use a decision tree to understand when to use 2D or 3D elements in either 2D or 3D analysis. In this context it is also crucial to understand what are the differences between surface and shell elements and where they are applied.

## Slide 31: 2D and 3D – Analysis and Elements
Model both in-plane and out-of-plane behavior.
They have both translational and rotational DoFs.
Account for thickness and its effects on bending.
More complex, where bending is important.
2D Elements
3D Elements
Surface
Shell
Solid
Plane Stress
Plane Strain
Thin structures in 3D
Thick structures in 3D*
3D analysis
2D analysis
Primarily model in-plane behavior only.
Typically, they have only translational DoFs.
Do not consider thickness or bending.
Simpler and used where only in-plane forces are relevant.
*Thick structures can also be considered using 2D, but usually solid elements are preferred.
Notes: Discretization – 1D, 2D and 3D elements
Since we already know that one of the first things to notice is the number of dimensions in space that we are working with, we will deepen into the possibility of using 2D and 3D elements in different types of analyses. In this slide, we have omitted 1D elements, since they will not be used in further explanations. To remember 1D-element analysis, check the previous lecture “Introduction to Finite Element Analysis (1D elements) with Ansys Mechanical”.
For 2D analysis, there is the possibility of working with 2D elements, but not with the solid ones. The 2D elements used for 2D analysis are called surface (or plate) elements and two main assumptions can be applied: the plane stress or the plain strain. The concept of plane stress and plane strain will be further discussed, as well as the axisymmetry These elements primarily model in-plane behavior only and have only translational DoFs. Because of that, they do not consider thickness or bending and are way simpler in terms of complexity and less computationally expensive.
There are, of course, positive things about choosing a 2D analysis, because 2D models are easier to design and faster to run. If one understands really well the physical problem and what happens in the other dimension – because, in real life, not just 2 dimensions are considered -, 2D models can be pretty accurate and effective. However, if out-of-plane behavior should be considered, it is necessary to go for a 3D analysis instead.
For 3D analysis, it is possible to use 2D or 3D elements, depending on the application.
The 2D elements used in 3D analysis are called shell elements and they model both in-plane and out-of-plane behavior, having both translational and rotational DoFs. Even if it is not physically represented in the geometry, they account thickness and its effects on bending, which makes the analysis more complex and computationally more expensive when compared to surface elements. Thus, shell elements are usually applied for thin-walled structures.
The 3D elements used in 3D analysis are called solid elements. This case is more expensive in terms of computational power, because it is necessary to create several elements through the geometry’s thickness to capture the physical reactions. They are usually reserved for problems that cannot be easily solved with 1D or 2D elements, such as thick structures – although they can also be considered using 2D, this is not the most common approach.
In the next slides, we will go through the theory of 2D and 3D elements and practice it with a couple of exercises to understand when to choose 2D or 3D analysis – and which elements should be applied in the mesh.
Next slide: Theory about 2D elements, with plane stress, plane strain and axisymmetric assumptions.

## Slide 32: 2D Elements – DoF and Theory
Hooke's law for small elastic deformations in isotropic materials
Plane Strain
All strains orthogonal to the chosen plane are zero. Considered when working with a thick structure. generally is not zero.
For X-Y-Plane:
Plane Stress
All stresses acting on the component are in the same plane and the stresses in the orthogonal direction are zero. Considered when working with a thin structure. generally is not zero.
For X-Y-Plane:
PLANE182
4 nodes
Axis symmetry
Axisymmetric behavior can be set instead of plane strain/stress behavior for plane elements using y as the symmetry axis. This assumption reduces 3D model to 2D, which decreases the calculation time.
In order to simplify 3D solid mechanics problems and treat them as a 2D project, there are some assumptions that can be used according to how the body responds to external loads (stress and strain).
PLANE183
8 or 6 nodes
Notes: 2D Place Elements – DoF and Theory
In order to simplify 3D solid mechanics problems and treat them as a 2D project, there are some assumptions that can be used according to how the body responds to external loads (stress and strain). These problems are governed by the generalized Hooke’s law, considering small deformations in an isotropic material. It can be written in a matrix notation using the elasticity matrix E. Taking this matrix as the starting point, we will discuss two main assumptions: Plane Strain and Plane Stress.
Plane Strain: All strains orthogonal to the chosen plane are zero. The out-of-plane stresses are not necessarily zero. This assumptions is often used while working with a thick structure.
Plain Stress: All stresses acting on the component are in the same plane and the stresses in the orthogonal direction are zero. The out-of-plane strains are not necessarily zero. Generally considered when working with a thin structure.
Finally, there is another assumption that can be set instead of plane strain/stress behavior for plane elements: the axis symmetry.
In general terms, symmetry means that a model is identical on both sides of a dividing plane (or line). When only a part of the model is used, additional boundary conditions must be added to avoid non-symmetric results due to the mesh. It means that the out-of-plane displacements and the in-plane rotations have to be zero.
Why to apply symmetry to a model? It reduces the model itself, such as number of nodes and elements, leading to a lower calculation time – a computationally less expensive simulation.
Thus, the Axial Symmetry is a type of symmetry where the symmetry is around a given axis. In Ansys environment, draw the geometry in the positive x-y plane where y is used as the axis of symmetry.
Next slide: The main exercise of this part of the lecture is the 2D plane stress analysis of a beam in bending.

## Slide 33: Task – Beam in Bending: 2D Plane Stress Analysis
Consider a beam of length 1 m made of structural steel under the following loading conditions. The cross-section of the beam is 100mmx100mm. Solve using a 2D plane stress analysis condition. (Reason: Stress in the z-direction can be assumed to be zero). Determine maximum deformation and stress.
1000mm
1kN/mm
450mm
450mm
x
y
100mm
Planar Approximations of a 2D Beam | Ansys Innovation Course
Notes: Task – Beam in Bending – Problem Statement
In the following slides, we will discuss the resolution of a classic problem of Solid Mechanics: a three-point flexural test. It is shown the drawing with the beam characteristics and the respective boundary conditions.
The beam has 1m of length and its cross-section is 100mmx100mm. The considered material is a structural steel.
The three-point flexural test consists in 2 fixed supports in each end and a distributed force of 1kN/mm applied vertically in a region of 100mm in the middle of the beam.
The goal is to run the simulation using a 2D plane stress condition, determining deformation and stress.
*Note: As we are assuming a 2D model, the thickness is considered as a property, and it is not physically modeled.
Next slide: We will discuss the procedure for using either the Ansys Workbench platform or Ansys Mechanical tool to run the simulation, by following the steps of importing the geometry, assigning the material, generating the mesh and defining boundary conditions.

## Slide 34: Beam in Bending: 2D Plane Stress Analysis - Procedure
2. Edit Properties of Geometry and change Analysis Type to 2D.
1. Create a Static Structural Analysis System in Ansys Workbench platform.
3. Create the geometry with the specified dimensions. It can be done in Discovery.
4. Open the model using Ansys Mechanical software and assign a thickness of 100mm.
5. Insert a Construction Geometry by right clicking on Model. Choose the Path option and create a path along the length and half of the width.
Notes: Task – Beam in Bending – Procedure
To start, after opening Ansys Workbench platform, we should create a Static Structural Analysis (1). Since we are working with Structural Steel (material by default), it is not necessary to edit the Engineering Data section.
Click on Geometry section with the right mouse button (RMB) and go to Properties, setting the Analysis Type to 2D (2). You can either import the geometry (the file is disponible for download) or create a new SpaceClaim or Discovery Geometry and start the sketch (3).
Open the model using Ansys Mechanical and, in the model tree, assign a thickness of 100mm in Geometry (4).
Go to Mesh and generate one using the Automatic Method (5).
After that, apply the boundary conditions in the Static Structural area of the model tree. Apply the fixed supports on the edges of the opposite sides and the force in the middle of the beam (6).
Choose the Total Deformation, Equivalent Elastic Strain, Normal Stress (X-Axis) and Equivalent von Mises Stress analysis and solve the model (7).
Next slide: We will discuss the results concerning the Total Deformation and Equivalent Elastic Strain analysis.

## Slide 35: Beam in Bending: 2D Plane Stress Analysis - Procedure
5. Generate a mesh with element size equals to 10mm
7. Solve
6. Insert a fixed support applied in the following 2 vertices.
7. For the loading condition, insert a force and define its components. The magnitude in the Y-Axis is 100kN in the opposite direction and there are not components in X and Z axes.
8. Insert two Directional Deformation analyses, both with Y-axis orientation. For the first one, choose the Scoping Method as Geometry Selection and, for the second, Path.
Notes: Task – Beam in Bending – Procedure
To start, after opening Ansys Workbench platform, we should create a Static Structural Analysis (1). Since we are working with Structural Steel (material by default), it is not necessary to edit the Engineering Data section.
Click on Geometry section with the right mouse button (RMB) and go to Properties, setting the Analysis Type to 2D (2). You can either import the geometry (the file is disponible for download) or create a new SpaceClaim or Discovery Geometry and start the sketch (3).
Open the model using Ansys Mechanical software and, in the model tree, assign a thickness of 100mm in Geometry (4).
Go to Mesh and generate one using the Automatic Method (5).
After that, apply the boundary conditions in the Static Structural area of the model tree. Apply the fixed supports on the edges of the opposite sides and the force in the middle of the beam (6).
Choose the Total Deformation, Equivalent Elastic Strain, Normal Stress (X-Axis) and Equivalent von Mises Stress analysis and solve the model (7).
Next slide: We will discuss the results concerning the Total Deformation and Equivalent Elastic Strain analysis.

## Slide 36: Beam in Bending: 2D Plane Stress Analysis - Results
Directional Deformation – Geometry Selection
Directional Deformation – Path
Notes: Task – Beam in Bending – Results: Directional Deformation
In a 3-point flexural test, it is necessary to understand the bending mechanics of the beam under the applied load. The beam is supported at two opposite vertices and the load is applied in an edge at the center, which creates a bending moment that is most intense at the center and decreases towards the supports.
As expected, the maximum deformation is in the middle of the beam. The opposite ends of the beam present zero deformation, since it is set fixed supports as boundary conditions. The beam bends into a curve known as “bending curve” or “deflection curve”.
To display the directional deformation along the path, we chose the neutral axis, where there is no strain (no deformation) in the Y direction.
Next slide: A similar analysis will be conducted to linearized von Mises Stress.

## Slide 37: Beam in Bending: 2D Plane Stress Analysis - Results
Equivalent von Mises Stress
Linearized Stress – Equivalent von Mises Stress
Product Documentation (ansys.com)
Notes: Task – Beam in Bending – Results: Equivalent von Mises Stress vs Linearized Equivalent Stress
In this analysis, it is possible to highlight the study of the neutral axis, which is an imaginary horizontal line through the center of the beam, where the structure experiences no longitudinal stress during bending.
Fibers located above the neutral axis are under compressive stress. On the other hand, fibers located below the neutral axis experience tensile stress. Thus, the maximum stress occurs at the furthest points from the neutral axis (at the top and bottom surfaces).
The stress is zero along the neutral axis.
Next slide: We will discuss a 2D analysis of an engineering application with a spherical pressure vessel.

## Slide 38: Pressure Vessel – Problem Statement
Consider a spherical pressure vessel with a cylindrical nozzle made of structural steel. The dimensions are given in millimeters. Run a 2D Axisymmetric analysis by defining the internal pressure load as 1.0 MPa. Determine Total Deformation, Equivalent and Normal stresses.
Static structural analysis using FEA of pressure vessel with Ansys Mechanical | Ansys Education Resources
Stresses in Pressure Vessels| Ansys Innovation Course
R200
R180
R30
R50
35
Notes: Task – Pressure Vessel – Problem Statement
2D analysis are often conducted with thin-walled structures. A very common example of this application are the pressure vessels, which can appear in different shapes and sizes.
For this exercise, consider a spherical pressure vessel with a cylindrical nozzle made of structural steel. In case you want to design the vessel by yourself, the dimensions are given in millimeters. The CAD file is also available for download and is attached to this lecture.
Run a 2D Axisymmetric analysis by defining the internal pressure load as 1.0 MPa and determine Total Deformation, Equivalent and Normal Stresses.
Next slide: We will discuss the procedure to run a Static Structural analysis on Ansys Workbench platform of the spherical pressure vessel.

## Slide 39: Pressure Vessel – Procedure
1. Create a Static Structural Analysis System in Ansys Workbench platform and import the geometry.
5. Proceed to set the boundary conditions.
4. Generate an Automatic Mesh with element size equals to 2.5mm.
2. Open the model in the Ansys Mechanical tool, go to Geometry and change the Dimension to 2D and the Behavior to Axisymmetric.
3. Add a Symmetry condition and set the Type as 2D Axisymmetric. Set the Number of Repetitions as 10 and the angle variation as 10°.
Notes: Task – Pressure Vessel – Procedure
First of all, create a Static Structural Analysis system in Ansys Workbench platform and import (or create) the geometry (1).
Open the model in the Ansys Mechanical tool and, in the Model Tree, go to Geometry and change the Dimension to 2D and the Behavior to Axisymmetric (2).
Right click on Model and create a symmetry condition. Set the Type as 2D AxiSymmetric, the Number of Repetitions as 10 and the Angle Variation as 10° (degrees) (3).
Generate an Automatic Mesh with element size equals to 2.5mm. It is already possible to see the symmetry condition (4).
Now, proceed to set the boundary and loading conditions for the problem (5).
Next slide: We will discuss how to set the boundary conditions and how to calculate the right loading conditions for this situation.

## Slide 40: Pressure Vessel – Procedure
6. In the internal edges of the pressure vessel, add a pressure load normal to the surface with 1 MPa of magnitude.
This blue region represents the pressure load on the nozzle top surface.
As a reaction, the force applied in the internal surface of the vessel is distributed on the nozzle top.
Top view
8. Add a displacement on the edge at the bottom of the vessel, fixing the Y and Z dimensions.
7. Calculate the pressure load to be applied in the nozzle top by using the given dimensions in the problem statement.
Notes: Task – Pressure Vessel – Procedure
As the first loading condition, add a pressure load (magnitude 1.0 MPa) normal to the internal edges of the vessel (6).
If we choose to observe the top view of the vessel, it is possible to see two regions: 1) The internal area under the 1.0 MPa pressure load, and 2) the nozzle top surface, which suffers the reaction of the internal pressure. To define this reaction, we will consider that the same force applied in the internal area of the vessel is equally distributed on the nozzle top surface.
Using the CAD dimensions given in the problem statement, it is possible to calculate the pressure load to be applied on the nozzle surface.
We will get a pressure load of magnitude equals to 0.562 MPa, normal to the surface, but in the opposite direction (7).
Finally, add a displacement condition to the internal edge on the bottom of the vessel, fixing the Y and Z directions, as shown (8).
Next slide: We will check the results for Total Deformation, Equivalent and Normal Stresses.

## Slide 41: Pressure Vessel – Results
Total Deformation [mm]
Equivalent Stress | von Mises Stress
Normal Stress – X-Axis [MPa]
Notes: Task – Pressure Vessel – Results
Total Deformation: The highest deformation occurs at the cylindrical nozzle.
Stresses: Similarly, the highest stresses values happen in the transition of the spherical geometry to the cylindrical nozzle.
The transition from the spherical part of the vessel to the cylindrical nozzle creates a discontinuity of the geometry, which can cause stress concentrations, amplifying the deformation – once the pressure acts uniformly on the spherical surface, but may interact differently with the nozzle.
Next slide: We will now discuss about 3D element analysis, highlighting the differences between a solid and a FE model.

## Slide 42: 3D FEA – Solid model and FE model
FE model
SOLID185
8 nodes
The FE model, made of nodes and elements, can be easily obtained from a solid model. Its boundary conditions are directly applied in the nodes.
SOLID186
SOLID187
20 nodes
10 nodes
Solid model
A model made of line, vertices, surfaces and volumes, which boundary conditions must be transformed from the solid geometry to the underlying nodes.
Solid model
FE model made up of solid elements
Notes: Solid model and FE model
In this slide, it is explained the differences between a solid model and a finite element (FE) model.
It is crucial to start the understanding of this topic by the fact that a solid model is not the same thing as a FE model made up of slid elements. *Click*
A solid model is made of lines, vertices, surfaces and volumes. Ansys uses SURF*** elements to transfer loads applied to the solid model to the FE model, once the boundary conditions must be transformed from the solid geometry to the underlying nodes. *Click twice*
A FE model is made of nodes and elements and, once you have a solid model, it is easy to obtain the FE one. The boundary conditions and directly applied in the nodes.
The solid elements we will discuss are SOLID185, SOLID 186 and SOLID 187. *Click*
The quadratic element SOLID185 is an 8-node-element, which can be used as a tetrahedral element. It presents 3 degrees of freedom (DoF) – Ux, Uy, Uz. *Click*
The quadratic element SOLID186 is a 20-node-element and also can be used as a tetrahedral element. It presents 3 degrees of freedom (DoF) – Ux, Uy, Uz. *Click*
The quadratic element SOLID87 is a 10-node-element and always has a tetrahedral shape. It presents 3 degrees of freedom (DoF) – Ux, Uy, Uz.
Later on this lecture, we will work with this bicycle frame geometry to run a 3D static structural analysis.
In the next slide, it is explained Elasticity and Stress-Strain Relationship, once 3D solid elements are employed to determine the state of stress.

## Slide 43: 3D FEA – Solid elements (Elasticity and Stress-Strain Relationship)
For any structure that cannot be adequately be represented or simplified using beam and shell elements, 3D solid elements are employed to determine the state of stress.
Stress-Strain Relationship
For linear-elastic behaviour, the most fundamental constitutive law, called Hooke’s law, is considered
y,v
x,u
z,w
y
x
z
Note : This is a depiction of the state of stress in a random 3D elastic body.
Introduction to Material Elasticity | Ansys Innovation Course
Theory of Elasticity
The property of solid material to deform under external force and return to its original shape after load is removed
Stress
Strain
Linear Elastic Material | Ansys Innovation Course
Notes: 3D FEA – Solid Elements (Elasticity and Stress-Strain Relationship)
For any structure that cannot be adequately be represented or simplified using beam and shell elements, 3D solid elements are employed to determine the state of stress.
Theory of Elasticity: It describes how solid materials deform and respond to external forces, returning to their original shape after the load is removed. The key principles are stress and strain.
Stress comes from external loads applied to the material and it is usually represented by a tensor with normal stress (σ) and shear stress (τ) components. Strain relates the deformation of the material compared to its original length and it is also represented by a tensor with normal strain (ԑ) and shear strain (ץ).
Stress-Strain Relationship: For linear-elastic behavior, the relationship between stress and strain in a material is described by the most fundamental constitutive law – the Hooke’s law, as we previously saw in 2D analysis. The stress tensor is inversely proportional to the strain tensor, where the related constant is the Young’s Modulus (E), a measure of stiffness. In simple words, the Young’s Modulus measures the material’s ability to resist to axial deformation.
  From the Young’s Modulus, it is possible to derive the equations of Shear Modulus (G) and Bulk Modulus (K) using the Poisson’s ratio (ν), which represents the ratio of transverse strain to axial strain. Thus, the Shear Modulus (G) measures the material’s ability to resist shear deformation, while the Bulk Modulus (K) measures the material’s ability to resist volumetric deformation.
Next slide: We will discuss about displacement field, equilibrium equations and strain-displacement relationship.

## Slide 44: 3D FEA – Solid elements (Elasticity and Stress-Strain Relationship)
Displacement Field
The displacement field captures the effect of deformation on the body and is defined by a displacement vector (position in reference to an origin)
Strain-Displacement Relationship
The partial derivatives express displacement gradients (rate of change in displacement) for small normal and shear strains
,
,
, i, j = 1,2,3
Strain in Deformation Analysis | Ansys Innovation Course
Equilibrium Equations
For elastostatic problems 3 equilibrium conditions with stresses and body forces must be satisfied
y,v
x,u
z,w
y
x
z
Note : This is a depiction of the state of stress in a random 3D elastic body.
Notes: 3D FEA – Solid elements (Elasticity and Stress-Strain Relationship)
Displacement Field: The displacement field captures the effect of deformation on the body and it is defined by a displacement vector (position in reference to an origin). In other words, the displacement field provides a description of how every point in the material moves as a result of these loads. For a 3D problem, the displacement field can be broken into three components, describing how the material deforms in each spatial direction.
Equilibrium Equations: In a 3D elastic body, the elastostatic equilibrium equations ensure that the internal stresses balance the external forces and moments. This comes from the principle of equilibrium, where the sum of forces and moments on a material must be zero.
Where is the divergent of the stress tensor and b the body force vector per unit volume.
In the previous lecture about Finite Element Analysis with 1D Elements, the theory of equilibrium is detailed. For further information, check those slides.
Strain-Displacement Relationship: The strain field measures how the deformation of the material changes relative to its original dimensions and it can be directly related to the displacement field.
For a 3D system, with displacements u, v and w, the relationship between strain and displacement is given by partial derivates that express displacement gradients for small normal (longitudinal and transverse , ) and shear (, and ) strains.
The strain tensor is symmetric, which means e.g. = , because the other of differentiation does not affect the result.
Next slide: We will run a 3D static structural analysis using the geometry of a simple wrench.
3D FEA – Solid elements (Elasticity and Stress-Strain Relationship)
Displacement Field: The displacement field captures the effect of deformation on the body and it is defined by a displacement vector (position in reference to an origin). In other words, the displacement field provides a description of how every point in the material moves as a result of these loads. For a 3D problem, the displacement field can be broken into three components, describing how the material deforms in each spatial direction.
Equilibrium Equations: In a 3D elastic body, the elastostatic equilibrium equations ensure that the internal stresses balance the external forces and moments. This comes from the principle of equilibrium, where the sum of forces and moments on a material must be zero.
∇⋅𝜎+𝑏=0
Where ∇⋅𝜎 is the divergent of the stress tensor and b the body force vector per unit volume.
In the previous lecture about Finite Element Analysis with 1D Elements, the theory of equilibrium is detailed. For further information, check those slides.
Strain-Displacement Relationship: The strain field measures how the deformation of the material changes relative to its original dimensions and it can be directly related to the displacement field.
For a 3D system, with displacements u, v and w, the relationship between strain and displacement is given by partial derivates that express displacement gradients for small normal (longitudinal 𝜀_𝑥𝑥 and transverse 𝜀_𝑦𝑦, 𝜀_𝑧𝑧) and shear (𝛾_𝑥𝑦, 𝛾_𝑥𝑧 and 𝛾_𝑦𝑧) strains.
The strain tensor is symmetric, which means e.g. 𝛾_𝑥𝑦 = 𝛾_𝑦𝑥, because the other of differentiation does not affect the result.
Next slide: We will run a 3D static structural analysis using the geometry of a simple wrench.

## Slide 45: Wrench: 3D Stress Analysis – Problem Statement
Consider a wrench that is used to tighten up a bolt with a force of 100N. It is made of cast iron under the following loading conditions. Solve using a 3D stress analysis condition. Determine maximum deformation and von Mises stress. Furthermore, conduct a mesh-convergence study and determined the mesh quality.
Force
Boundary conditions
Note: The CAD file is attached: Wrench.scdoc
Notes: Wrench: 3D Analysis – Problem Statement
The first example of a 3D model simulation is using the geometry of a wrench. The CAD file is available for download.
Consider a wrench, made of cast iron, that is used to tighten up a bolt with a force of 100N. The boundary conditions are shown in the slide – a fixed support in the surfaces inside the head and a distributed force in the back of the shaft. The goal is to conduct a 3D stress analysis, determining maximum deformation and von Mises stress.
To study the mesh quality, we will conduct a parametrization and a mesh convergence study.
Next slide: We will discuss the workflow to conduct the simulation, starting with choosing the material and importing the geometry.

## Slide 46: Wrench: 3D Stress Analysis – Procedure
1. Create a Static Structural Analysis System in Ansys Workbench platform
2. Open the Engineering Materials and select ‘General Materials’ in the Engineering Data Source table. Then, add ‘Grey Cast Iron’ to your Engineering Data by clicking the plus icon and close the engineering data table.
3. Import the wrench geometry (Wrench.scdoc) that is attached to this document and open the model using the Ansys Mechanical module.
Notes: Wrench: 3D Analysis – Procedure
After opening the Ansys Workbench platform environment, create a Static Structural Analysis (1) and open the Engineering Data.
In Engineering Data Sources table, look for ‘General Materials’ and add Grey Cast Iron by clicking the plus icon (2).
Go back to the project on the Ansys Workbench platform, import the geometry file that is attached to this document and open the model using the Ansys Mechanical module(3).
Next slide: We will continue with the workflow to run the simulation, explaining about how to assign a material, generate a mesh and apply boundary conditions.

## Slide 47: Wrench: 3D Stress Analysis – Procedure
5. Generate a mesh with the automatic method and an element size of 10 mm
4. Select the solid geometry in the Model Tree and assign ‘Grey Cast Iron’ to the wrench.
7. Apply a force of 100N at the dedicated section at the back of the wrench
6. Apply a fixed boundary condition at the tool head (internal faces)
Notes: Wrench: 3D Analysis – Procedure
After opening the model in the Ansys Mechanical tool, select the solid geometry in the Model Tree and assign the material that was previously added – Grey Cast Iron (4).
With that, we can generate the mesh and create the FE model (5). The mesh method that was chosen was the Automatic with an element size equals to 10mm.
In the Model Tree, going to the Static Structural section, insert the specified boundary conditions – a fixed support in the three internal surfaces of the tool head (6) and a distributed force of 100N at the dedicated section at the back of the wrench (7).
Next slide: After creating the analysis at the Solution section, we will discuss the results of Total Deformation and Equivalent von Mises Stress.

## Slide 48: Wrench: 3D Stress Analysis – Results
Total Deformation [mm]
Note: This analysis was conducted with the automatic meshing method and an element size of 10 mm.
Equivalent von Mises Stress [MPa]
Very coarse and rough stress distribution across elements indicates insufficient mesh refinement
Notes: Wrench: 3D Analysis – Total Deformation and Equivalent von Mises Stress results
Total Deformation:
  The region that presents no deformation is the tool head, where we defined the fixed support in the internal surfaces. The maximum deformation is localized on the other end of the wrench, where the force is applied. It is possible to see the tendence of deformation in the video on the right top of the slide.
Equivalent von Mises Stress:
  The highest values of equivalent stress are concentrated in the connection between the tool head and the shaft. This can happen because of the abrupt change of the geometry (the cross-sectional areas) where the forces are transmitted from the head to the shaft. The beginning of the wrench shaft experience the combined effects of the applied force at the back and the reaction force of the fixed support. There is also significant bending and shear stresses.
  It is possible to observe that the chosen element size (10 mm) produces a very coarse mesh, causing rough stress distribution. It indicates insufficient mesh refinement, and it is necessary to improve it so the solution can be more accurate.
Next slide: A parametrization study will be conduct. The input parameter is the element size and the output parameters are the results of total deformation and equivalent von Mises stress.

## Slide 49: Wrench: 3D Stress Analysis – Parametrization
1. Select the box on the left side of Element Size to set it as a parameter.
2. At the Results section, repeat it for the maximum values of Total Deformation and Equivalent Stress.
3. The Parameter Set tab will appear in the menu. Open in and duplicate the parameter to create as many as you want to analyze.
4. Choose different values for the Mesh Element Size and update the selected design points. The stress and deformation results will be calculated.
5. Grab Response Surface in the Design Exploration region in the Ansys Workbench platform.
Notes: Wrench: 3D Analysis – Parametrization study
We saw in the last slides how important it is to have a good mesh quality to achieve accurate solutions. However, the results from the simulation of the wrench model were not optimized, since the mesh was quite coarse. In order to improve the mesh quality by changing the element size, we will conduct a parametrization study to understand how the solution varies.
To start, still in the Ansys Mechanical interface, choose Element Size as an input parameter by clicking the white box on the left of the name (1). If a blue P appears, this value is already considered as a parameter. At the Results section, repeat it for the maximum values of Total Deformation and Equivalent von Mises Stress (2).
On the Ansys Workbench environment, a Parameter Set section will appear after defining the input and output parameters for the project. Open this section and duplicate the existing parameter as many times as you want (3). Choose different values for the Mesh Element Size and update the selected design points (4). The equivalent stress and the total deformation results will be calculated.
Again the Ansys Workbench environment, grab in the Toolbox the Response Surface, which is part of the Design Exploration section (5).
Next slide: We will discuss the graph generated with the previously chosen parameters and compare the differences between the results of Total Deformation and Equivalent von Mises Stress.

## Slide 50: Wrench: 3D Stress Analysis – Parametrization
6. Open Design of Experiments and, in the Charts option, open Design Points vs Parameter.
7. For the Y-Axis, choose Equivalent Stress to display on the left and Total Deformation to display on the right. For the X-Axis, display the design points.
Notes: Wrench: 3D Analysis – Parametrization study
Open the Design of Experiments in the Response Surface group and, in the Charts section, open Design Points vs Parameter (6). For the Y-Axis, choose Equivalent Stress to display on the left and Total Deformation to display on the right. For the X-Axis, display the design point – which are the points created with the new values of the mesh element size (7). In this slide, it is possible to see the variation of these results according to the changes of the element size. The stresses are displayed in MPa, and the deformation is expressed in millimeters.
Next slide: A convergence study will the conducted with the number of Mesh Nodes for the X-Axis and the Equivalent Stress for the Y-Axis.

## Slide 51: Wrench: 3D Stress Analysis – Convergence Study
1. In the Parameters section, open Charts and choose Parameters Chart.
2. For the X-Axis, choose the number of Mesh Nodes and, for the Y-Axis, choose the Maximum Equivalent Stress results.
3. Start with a very coarse mesh (25mm) and refine the mesh to an element size equal to 2.5mm by duplicating design points. The output parameters are the mesh nodes and the maximum equivalent stress values.
4. The study led to a convergence of stress result to a finite value. After reaching 10000 elements, the mesh does not need to be refined anymore. Thus, for an accurate solution, one should choose an element size equal to 2mm (5 times less than the initial guess).
Notes: Wrench: 3D Analysis – Convergence study
Come back to the model in the Ansys Mechanical software and set the number of Mesh Nodes as a parameter. After that, open the Parameters section, go to Charts and choose Parameters Chart (1).
For the X-Axis, choose the number of Mesh nodes and, for the Y-Axis, choose the Maximum Equivalent Stress results (2).
Duplicate the design points to recalculate the results. Start with a very coarse mesh (25mm) and refine it to an element size equal to 2.5mm (12 design points total) (3).
The chart that will be plotted allows us to proceed with a convergence study. As we saw on slide 15, the mesh converges when the stress results do not change significantly when the element size varies. If the model has stress singularities, the curve will show a divergence – to remember the concepts of stress singularities, come back to slide 20.

## Slide 52: Bike frame: 3D Analysis – Problem Statement
Consider the bike frame below. It is made of aluminum alloy under the following conditions. The cyclist’s weight is 115 kg. Solve using a 3D stress analysis condition. Determine maximum deformation and von Mises stress.
Note: The CAD file is attached: bikeframe.scdoc
Notes: 3D Analysis of a Bike Frame – Problem Statement
Consider the 3D model of a bike frame made of aluminum alloy under specified boundary and loading conditions.
There are two fixed supports, one at the back fork and the other at the headset. The bike frame is also under the standard earth gravity and the representation of the cyclist is the point mass at the saddle. Consider a cyclist with 115kg.
Solving as a 3D analysis, determine the deformation and the equivalent von Mises stress.
Next slide: We will discuss the workflow to run the simulation of this geometry, starting with importing the file, generating the mesh and setting the respective boundary conditions.

## Slide 53: Bike frame: 3D Analysis – Procedure
2. In Engineering Materials, add ‘Aluminum Alloy’ to the Engineering Data. Import the geometry bikeframe.dsco and open the model using the Ansys Mechanical software.
3. Assign ‘Aluminum Alloy’ to the geometry and generate a mesh with the automatic method and an element size of 10 mm.
4. Apply the boundary conditions previously mentioned.
5. Solve
1. Create a Static Structural Analysis System in Ansys Workbench platform
Notes: 3D Analysis of a Bike Frame – Procedure
After opening Ansys Workbench platform, create a Static Structural Analysis and open the Engineering Data section (1). In Engineering Data Sources, select the General Materials library and add the Aluminum Alloy (2). Come back to the project, import the geometry (which file is available for download) and open the model.
With the Ansys Mechanical tool open, assign “Aluminum Alloy” as the material for the geometry and generate an Automatic mesh with element size equals to 10mm (3). Apply the boundary conditions previously mentioned (4).
In the model tree, in Static Structural section, add the analysis of Total Deformation and Equivalent von Mises Stress. Run the simulation (5).
Next slide: We will discuss the results of deformation and stress that were generated in this analysis.

## Slide 54: Bike frame: 3D Analysis – Results
Total Deformation [mm]
Equivalent von Mises Stress [MPa]
Notes: 3D Analysis of a Bike Frame – Total Deformation and Equivalent von Mises stress results
Total Deformation:
  It is possible to see that the highest deformation is localized on the rear part of the frame. This area has to support traction and compression forces coming from the drivetrain response to the terrain. This results can vary according to the frame design, the weight distribution and the material stiffness, for example. The boundary conditions also influence the model response.
  One may try to set different boundary conditions (different fixed supports and values for the point mass), as well as changing the material (to steel or to carbon fiber, for example), to check how the results can change according to the understanding of the physical problem.
Equivalent von Mises Stress:
  The highest values for von Mises stress are localized in some specific points:
    On the rear triangle, specially around the junctions where the chain stays connect to the rear dropout and where the seat stays connect to the top tube.
    On the bottom bracket area, where the tunes connect with the crankset. This region experiences high forces from pedaling and torque, making a point of stress concentration.
    On the dropout, where the rear wheel is connected, which are subject to stresses from braking and drivetrain torque.
In real life, the bike frame is subject to dynamic conditions and the static structural analysis may not provide the most accurate results, but one can have an idea of how the structure responds under certain conditions.
Next slide: We will discuss the workflow to run a modal analysis in order to understand the frequency modes.

## Slide 55: Bike frame: 3D Analysis – Modal Analysis
1. Create a Modal Analysis System in Ansys Workbench platform and link the solution of the Static Structural to the model of the Modal.
2. In Analysis Setting, define the maximum number of modes to be found.
3. In Solution, create a Total Deformation analysis for each mode you have found.
4. Analyze each mode.
The graph plots the frequency and its respective mode.
Notes: 3D Analysis of a Bike Frame – Modal Analysis (Frequency Modes)
To run a modal analysis in this example can be important for several reasons. It helps determine the natural frequencies at which the bike frame will tend to vibrate. By knowing them, one can ensure that this geometry will not resonate with external forces that could cause excessive vibrations – and discomfort for the cyclist.
Also, if any mode of vibration is problematic, it is possible to optimize the design or the material distribution in order to reduce stress concentrations. This is essential not only to ensure the cyclist’s comfort, but also their security, avoiding irreversible deformations and structural failures.
That said, come back to the project tab on Ansys Workbench platform and create a Modal Analysis. Link the solution of the Static Structural to the model of the Modal Analysis and open it (1). Choose the number of frequency modes to be found (2).
In the model tree, create a Total Deformation analysis for each mode you have found. In this example, we are working with 6 frequency modes, so there will be 6 deformation analysis (3). In each analysis, choose the number of the frequency mode (from 1 to 6, for example), so it is possible to check all the modes (4).
The animation shows the fourth frequency mode where the maximum deformation is equal to 6.3326mm. The graph plots the value of the frequency and its respective mode of vibration.
Next slide: This is the last example of the lecture. After that, we will summarize the topics of the lecture in a few sentences.

## Slide 56: Summary
Finite element analysis (FEA) is cost effective and saves time from design conception to manufacturing the component.
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies (elements). They can be used as surface or solid elements to develop 2D or 3D analysis, respectively.
In this lecture, we discussed the key concepts to generate a mesh, e.g. element shape and order. The choice of inappropriate mesh method can lead to the creation of wedge and pyramidal elements, decreasing the mesh quality.
The mesh quality is very important to achieve accurate solutions. For more complex geometries, it is often needed to refine the mesh, aiming the so-called mesh independence. For that, a convergence study is conducted.
2D elements can be differentiated into plane-strain as well as plane-stress elements and are considered when dealing with thick and thin structures, respectively.
2D elements can be used to simulate simple structures in 2D and 3D space, whereas 3D elements are used analyze more complex structures (i.e. cannot be accurately represented by 2D elements) in 3D space only.
Ansys Mechanical software has been used to solve 2D and 3D element problems ranging from a simple (e.g. dog-bone specimen) to a more complex (e.g. bicycle frame) system.
Notes: Summary
Finite element analysis (FEA) is cost effective and saves time from design conception to manufacturing the component. At the core of FEA lies discretization, which means a model is divided into a finite number of small bodies (elements). They can be used as surface or solid elements to develop 2D or 3D analysis, respectively. In this lecture, we focus on linear static structural problems using surface and solid elements.
We discussed about key concepts to generate a mesh, e.g. element shape and order. The choice of inappropriate mesh method can lead to the creation of wedge and pyramidal elements, decreasing the mesh quality – which can be measured by defined mesh metrics.
The mesh quality is very important to achieve accurate solutions. For more complex geometries, it is often needed to refine the mesh, aiming the so-called mesh independence. For that, a convergence study is conducted – which consists in decreasing the element size to the point the stress results do not change significantly anymore.
For 2D models, one dimension is considered significantly smaller than the other two, which may cause differences in the results of stress distribution, once it is not possible to evaluate through-thickness stress in surfaces. This approach is often chosen for thin-walled structures.
Ansys Mechanical software has been used to solve 2D and 3D element problems ranging from a simple (like a dog-bone specimen) to a more complex (like a bicycle frame) system.
Next slide: Further information and resources to this and other relevant topics are linked in the next slide.

## Slide 57: Further Information and Resources
  Ansys Academic | Simulation Software for Educators, Researchers and Students.
  Ansys Innovation Courses : Free to Access to courses covering a variety of physics and software.
  Ansys Education Resources: Specifically developed for Educators.
  Ansys Discovery Forum: Learn Discovery through video-tutorials.
  Ansys Learning Forum: Ask questions to the Ansys Community!
  Ansys Learning : Ansys YouTube Channel with dedicated video playlists.

## Slide 58: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5