## Slide 1
Lab Tutorial on Radar example using Ansys HFSS™ SBR+ Simulation
Dimitris Tzagkas Celia Gomez Molina
education@ansys.com

## Slide 2: Received Power for Comms scenario
Assumptions:
Tx and Rx Antennas are impedance-matched
Tx and Rx Antennas are polarization-matched
Tx and Rx Antenna radiation efficiency is 1
where
Radar Equation
Radar system
Transmitter Antenna (Tx)
Receiver Antenna (Rx)
Incident wave propagation path
Reflected wave propagation path
Radar Target
Radar Target reflects / re-emits incident radar signal
Power intercepted and reflected from target
Power density at receiving antenna
Power transmitted
Power received
Notes: In this slide you can see the equations used to reach the radar range equation. The equations use the transmit power, the power density and the antenna parameters such as the gain (G) and the directivity (D).

## Slide 3: How to simulate the setup with Ansys HFSS SBR+
Parameters used:
Antenna model(s) in HFSS
  Identical Horn Antenna at ,
  with efficiency ,
  with maximum gain at boresight of 20.92 (13.2 dB),
  excitation power
Link and Setup configuration
  Radar consists of receiver and transmitter antennas that are at the same location
  Identical horn antennas for transmitter and receiver,
  Target sphere is at the boresight of the antennas with radius of 0.5m
  Variable distance between them R
Tx/Rx
Target
R
This tutorial uses Ansys HFSS™, the high-frequency electromagnetic simulation software

## Slide 4: Radar equation scenario implemented in Ansys HFSS software
Radar received power level depending on the distance of the target sphere

## Slide 5
How to create a radar scenario in Ansys HFSS Software

## Slide 6: Antenna Design
Use an existing antenna OR generate using the ACT Antenna Toolkit in Ansys HFSS: View ACT Extensions  Launch Wizards HFSS Antenna Toolkit  Any Antenna needed  Set parameters Synthesis  Finish The example next uses a pyramidal Horn Antenna at 2.4 GHz center frequency.
Excitations (right click)  Set Far-Field Phase Reference..
And then set a Far-Field Phase Reference point for the antenna.

## Slide 7: Analyze Antenna
Make sure Save Fields is checked…… Setup Freq Sweep ... and… Analyze
Step A
Step B
Step C
You can set sweep to specific frequencies OR even a single specific frequency

## Slide 8: Antenna Parameters extraction
From Excitations we can set the input power [1 W in this case]
From Results we can get the Total Gain [20.9 or 13.2 dB]

## Slide 9: Antennas for radar case
For the example you can either
  Use the existing horn antenna created and analyzed for the previous project (this method is used in the current presentation)
  OR
  Create a new/different antenna OR load antenna parameters from different project

## Slide 10: Setting Up the System Setup
Create New HFSS Design
Change Solution Type to SBR+
Create Antenna Component via Link to Source Design..
Name Appropriately the Antenna

## Slide 11: Setup Link – Working in the SBR+ design now
General Tab
Model Visualization Tab
OK, Next and Finish
Make sure you choose the correct Sweep

## Slide 12: Linking the Receiver Antenna …
Change Units to appropriate scale..
Add Receiving antenna (Radar_Rx) at the same location of the Transmitting Antenna
Name Appropriately the Antenna
AND REPEAT THE SAME AS FOR THE Rx ANTENNA

## Slide 13: Adding the target coordinate system…
Change Units to appropriate scale..
Add parametric Relative Coordinate System ..
* R1 = 10 meter
You can add the Relative CS anywhere and then modify the attributes as shown below

## Slide 14: Adding the target at the Relative Coordinate System reference
Select the RelativeCS1 and then draw a sphere as a target When done  you will get the below setup
The sphere can be placed anywhere and then modify properties as here:

## Slide 15: Assign Tx and Rx behaviors
Assign port and behavior type as shown below

## Slide 16: Excitation setup
From Excitations we can set the input power [1 W in this case]
In a radar system there are 2 antennas: a) the transmit (Tx) antenna and b) the receive (Rx) antenna
Unless time-separated, the receive antenna receives the target-reflected signals but also the direct signal from the transmit antenna (unwanted).
In Ansys HFSS software, we can reject the direct transmitted signal (from Tx antenna) by selecting the Field Type to be the “Scattered from SBR+ Regions” (see below).
Radar system
Transmitter Antenna
Receiver Antenna

## Slide 17: Setup Analysis and Run Analysis

## Slide 18: Analyze for different distance R1
Add Parametric setup for R1
You can define the start/stop/step accordingly. More steps mean more simulation time

## Slide 19: Plotting results

## Slide 20: Results – Compared to calculated radar equation (imported)
Radar received power level depending on the distance of the target sphere
Notes: For a comparison side by side you can export the simulation data OR import the calculated theoretical data in order to compare the simulated and calculated data in a single graph. In this example the calculated data are imported in HFSS

## Slide 21: Creating animated picture
OR
THEN

## Slide 22: Creating animated picture
Setup animation and steps
Animate
Export (*.avi OR *.gif file)

## Slide 23: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5